## Slide 1: Licensed Process for Disposal of Low-Activity Wastes in the WCS RCRA Cell Chris Shaw – May 2018 Corporate RSO & TSPM

## Slide 2: What is Low Activity Waste (LAW) Disposal?
Process Authorized by the WCS Radioactive Materials License
  Allows disposal in the WCS RCRA cell
  Approved by the TCEQ
  Low-Activity Class A Waste, not a New Waste Type
  TCEQ Approval Process Specified in 30 TAC 336.5 is similar to 10 CFR 61.6, and is at least as restrictive as 10 CFR 20.2002 exemption process.

## Slide 3: WCS LAW Disposal
Low Activity Waste Disposal
  Also referred to as LC 192 disposal (the license condition under Radioactive Materials License R04100 authorizing exemption)
  Controlled by the procedure RS-5.0.0 process for waste profiling, characterization, verification, and approval.

## Slide 4: WCS LAW Disposal
What are the Advantages of LAW Disposal?
  Lower cost compared to Class A disposal in a licensed disposal facility
  Waste concentrations up to Approximately 10% of the Class A limit are acceptable for disposal
  Estimated to represent a range of 80% to 95% of decommissioning waste volumes

## Slide 5: WCS LAW Disposal
Is the Generator Required to Submit an Import Application for LAW Disposal?
  No – The RCRA/TSCA cell is not a Compact facility
  Both Federal and Commercial wastes are accepted
  RCRA cell stewardship is the responsibility of WCS

## Slide 6: WCS LAW Disposal
Is it Necessary to Register with the Texas DSHS, or Become a WCS-approved Generator?
  No - DSHS Registration and WCS Audit/Approval process apply only to CWF & FWF generators
  Disposal of LAW requires WCS review and approval of a detailed waste profile supported by direct sampling and analysis

## Slide 7: WCS LAW Disposal
Only two types of characterization are acceptable for this process:
  Approved Laboratory Data from approved labs as per 30 TAC §25.2
  Non-Destructive Analysis (NDA) e.g. High Purity Germanium Detectors. Typical for debris that cannot be sampled with isotopic distributions that lend themselves to this type of analysis.

## Slide 8: WCS LAW Disposal
Additional Services at WCS
WCS can perform NDA characterization upon receipt.
Waste sorting and segregation to remove prohibited items and separate higher activity waste for CWF disposal
Packaging and transportation
Characterization and profiling

## Slide 9: WCS LAW Disposal
Additional Services
WCS has established subcontracts with Alaron & Omega, providing a suite of options for generators, including:
  Waste sorting and segregation to remove prohibited items and separate higher activity waste for CWF disposal
  Packaging and transportation
  Characterization and profiling

## Slide 10: WCS LAW Disposal
Any other Waste Requirements?
  The waste stream is homogenous in physical form and isotopic concentration
  Disposal is in a RCRA cell, so LDR-compliant mixed wastes can be accepted
  More than one profile may be required for a given waste type based on the concentration Tier and material density

## Slide 11: WCS LAW Disposal
What are the Waste Tiers?
  The requirements for WCS verification become more stringent as the concentration limits for disposal are approached.
  These waste Tiers are:
    Up to 30% of exemption limit – Tier 1
    30% - 80% of exemption limit – Tier 2
    80% - 100% of exemption limit – Tier 3
    All waste designated as DU is Tier 3 regardless of concentration

## Slide 12: WCS LAW Disposal
More on Waste Tiers
Tiers also affect the process for regulator review and approval of the waste exemption
    Tier 1 and 2: WCS Exempts the waste and provides information packages to TCEQ within 5 days of disposal
    Tier 3: Exemption concurrence from TCEQ is required before disposal (typically less than a week, 21 days allowed by license)

## Slide 13: WCS LAW Disposal
What Are the Low Activity Concentration Limits?
  RS-5.0.0 contains a table of isotopic concentrations for wastes, to which the sum of fractions rule applies
  Example isotopic limits:
    U-238: 23,000 pCi/g
    Sr-90: 2,500 pCi/g
    H-3: 50,000 pCi/g

## Slide 14: WCS LAW Disposal
What Other Limits Apply?
ALARA and Administrative Limits also apply:
    75 mR/hr maximum contact dose of any discrete item within a package

## Slide 15: WCS LAW Disposal
Miscellany
  Activated metals are eligible for LAW disposal, subject to the concentration and dose limits
  SNM exemption concentration limits apply
  Acceptance of waste characterized predominantly by hard to detects may require WCS to send samples offsite for analysis
  Generators do not need to pursue any separate regulatory approval to use the LAW disposal process; it is a licensed activity

## Slide 16: WCS LAW Disposal
Summary
  Characterization requirements for the process are different from, and in some ways more stringent than those for disposal in a facility licensed for Class A waste.
  For low-activity wastes that qualify - WCS LAW disposal in the RCRA cell is a compliant, safe, and cost-effective disposal option.

## Slide 17: WCS LAW Disposal
Questions?
Chris Shaw
WCS Integrated Services
cshaw@wcstexas.com
214-313-2571