## Slide 1: RCRA Requirements for Land-Based Units
Charles Brown, P.G.
Michael Pimentel, P.E.
Industrial and Hazardous Waste Permits Section
May 15, 2018
Notes: RCRA Requirements for Land-Based Units
Charles Brown, P.G.
Michael Pimentel, P.E.
Industrial and Hazardous Waste Permits Section
May 15, 2018
<Alt Text> Picture of land based unit in background of slide theme

## Slide 2: Outline
Land Disposal Restrictions (LDR’s)
Types of Land-Based Units (LBUs)
RCRA and State Requirements
Notes: Types of Land-Based Units (LBUs)
RCRA and State Requirements
Land Disposal Restrictions (LDR’s)

## Slide 3: Types of Land-Based Units
Surface Impoundments
Waste Piles
Land Treatment Units
Landfills
Corrective Action Management Units (CAMU)
Notes: Types of Land-Based Units (LBUs)
RCRA and State Requirements
Land Disposal Restrictions (LDR’s)

## Slide 4: Land Based Units in Texas
Chart: Land-Based Units vs. Non Land-Based Units
| Land-Based Units | Non Land-Based Units
 | 406 | 1309
Chart: Types of Land-Based Units
| Surface Impoundments | Waste Piles | Land Treatment Units | Landfills
 | 179 | 6 | 24 | 94
Notes: <ALT TEXT>Graphics of breakdown of land based units:
76% of permitted units are not land based.
Second graphic land based units breakdown by unit type: 31% landfills, 59% Surface impoundments, 8% Land Treatment Units. 2% Waste Piles
Date is approximate based on latest available information.
Surface impoundments counted based on original permit status. Surface Impoundments may be closed as a landfill.

## Slide 5: Requirements and Standards
40 CFR Part 264 and 30 TAC Chapter 335
Location Standards
Design Standards
Operation Standards
Closure Standards
Post-Closure Care Standards
Notes: Requirements and Standards
40 CFR Part 264 and 30 TAC Chapter 335
Location Standards
Design Standards
Operation Standards
Closure Standards
Post-Closure Care Standards

## Slide 6: RCRA Requirements
40 CFR Part 264
  Subpart B – General Facility Requirements
  Subpart K – Surface Impoundments
  Subpart L – Waste Piles
  Subpart M – Land Treatment Units
  Subpart N – Landfills
  Subpart S – Special Provisions for Clean-up
Notes: RCRA Requirements
40 CFR Part 264
  Subpart B – General Facility Requirements
  Subpart K – Surface Impoundments
  Subpart L – Waste Piles
  Subpart M – Land Treatment Units
  Subpart N – Landfills
  Subpart S – Special Provisions for Clean-up

## Slide 7: Land Disposal Restrictions (LDRs)
40 CFR 268
Apply to waste that is land disposed
  Surface Impoundments
  Waste Piles
  Landfills
  Land treatment units
  NOT APPLICABLE to CAMU’s
All waste must meet LDRs prior to disposal
Notes: Land Disposal Restrictions (LDRs)
40 CFR 268
Apply to waste that is land disposed
  Surface Impoundments
  Waste Piles
  Landfills
  Land treatment units
  NOT APPLICABLE to CAMU’s – waste from remediation activities
All waste must meet LDRs prior to disposal

## Slide 8: Location Standards (40 CFR Part 268)
Seismic Considerations
  Not within 200ft of a fault with displacement in the Holocene
Floodplains
  Must be designed to prevent washout from 100-year flood
Salt Formations
  Liquids prohibited
Notes: Location Standards (40 CFR Part 268)
Seismic Considerations
  Not within 200ft of a fault with displacement in the Holocene – Last 10,000 years
Floodplains
  Must be designed to prevent washout from 100-year flood
Salt Formations
  Liquids prohibited

## Slide 9: Location Standards (30 TAC 335, Subchapter G)
Unsuitable Site Characteristics
  With 100-yr floodplains
  Wetlands
  Recharge zone of sole-source aquifer
    Edwards Aquifer in Texas
  Landfills may not overlie a regional aquifer unless
    Evaporation exceeds precipitation by >40 inches
    depth to groundwater is >100 feet
    10 feet of low permeability material beneath landfill containment structure and regional aquifer
Notes: Location Standards (30 TAC 335, Subchapter G)
Unsuitable Site Characteristics
  Within 100-yr flood plain
  Additional requirements to allow construction
  Wetlands
  Recharge zone of sole-source aquifer
  Landfills may not overlie a regional aquifer unless
    Annual evaporation exceeds precipitation by >40 inches and depth to groundwater is >100 feet
    10 feet of low permeability material beneath landfill containment structure and regional aquifer

## Slide 10: Location Standards (30 TAC 335, Subchapter G)
LBUs may not be located:
  Where soil units within 5ft of the containment structure have a Unified Soil Classification of GW, GP, GM, GC, SW, SP, or SM, or a permeability greater than 10-5 cm/sec
  Exceptions:
    Evaporation exceeds rainfall by more than 40 inches
    The soil unit does not provide a pathway for waste migration.
Notes: Location Standards (30 TAC 335, Subchapter G)
LBUs may not be located:
  Where soil units within 5ft of the containment structure have a Unified Soil Classification of GW, GP, GM, GC, SW, SP, or SM, or a permeability greater than 10-5 cm/sec
  Exceptions:
    Where the average annual evaporation exceeds average annual rainfall by more than 40 inches
    Based on most recent available data
    The soil unit is not sufficiently thick and laterally continuous to provide a significant pathway for waste migration.
    Determined by a qualified and licensed P.G.

## Slide 11: Location Standards (30 TAC 335, Subchapter G)
An LBU may not be located in areas of active geologic processes.
  unless designed, constructed and operated to prevent adverse effects
Notes: Location Standards (30 TAC 335, Subchapter G)
An LBU may not be located in areas of active geologic processes.
  unless designed, constructed and operated to prevent adverse effects resulting from the geologic processes.
  Geological process may include, but not limited to – Active Subsidence, Mass wasting (soil creep, landslides), Seismic activity, volcanic activity
<Alt Text> Pictures of a landslide and lavaflow

## Slide 12: Location Standards (30 TAC 335, Subchapter G)
In areas protected by a barrier island or peninsula
Within 1,000 ft. of an area subject to active coastal shoreline erosion.
    unless designed, constructed and operated to prevent adverse effects resulting from storm surges or scouring.
Notes: Location Standards (30 TAC 335, Subchapter G)
In areas protected by a barrier island or peninsula
  An LBU may not be located within 1,000 ft. of an area subject to active coastal shoreline erosion.
    unless designed, constructed and operated to prevent adverse effects resulting from storm surges or scouring.

## Slide 13: Location Standards (30 TAC 335, Subchapter G)
An LBU may not be located near a fault
  Within 30 feet of the upthrown side
  Within 50 feet of the downthrown side
  Actual or inferred surface expression
  Demonstrated displacement of shallow Quaternary sediments or man-made structures
  unless designed, constructed and operated to prevent adverse effects resulting from fault motion
Notes: Location Standards (30 TAC 335, Subchapter G)
An LBU may not be located near a fault – inactive or not
  within 30 feet of the upthrown side
  within 50 feet of the downthrown side
  actual or inferred surface expression
  Demonstrated displacement of shallow Quaternary (2.5 Ma) sediments or man-made structures
  unless designed, constructed and operated to prevent adverse effects resulting from fault motion

## Slide 14: Surface Impoundments
Design and Operational Requirement's
  40 CFR Subpart K and 335.168
Liner Systems (after July 29, 1992)
  Top Liner (geomembrane)
  Leachate Collection System (LCS)/Leak Detection System (LDS)
    k = 10-1 cm/sec
    Typically sand/gravel or geonet
Notes: Surface Impoundments
Design and Operational Requirement's
  40 CFR Subpart K and 335.168
Liner Systems (after July 29, 1992)
  Top Liner (geomembrane)
  Leachate Collection System (LCS)/Leak Detection System (LDS)
    k = 10-1 cm/sec
Typically sand/gravel or geonet

## Slide 15: Surface Impoundments
Liner Systems (after July 29, 1992)
  Composite bottom liner
    Upper component – geomembrane
    Lower component – compacted clay
      3 feet thickness
      k less than/equal to 10-7 cm/sec
Notes: Surface Impoundments
Liner Systems (after July 29, 1992)
  Composite bottom liner
    Upper component – geomembrane – 60mil HDPE
    Lower component – compacted clay
      3 feet thickness
      k less than/equal to 10-7 cm/sec

## Slide 16: Surface Impoundments
Action Leakage Rate
  Maximum design flow rate that LDS can remove without the fluid head on the bottom liner thickness of drainage media.
    Average daily flow rate for each sump (gallons per acre per day)
    Calculated weekly during active life and closure period, monthly during post-closure care
Notes: Surface Impoundments
Action Leakage Rate
  Maximum design flow rate that LDS can remove without the fluid head on the bottom liner thickness of drainage media
    Average daily flow rate for each sump (gallons per acre per day)
    Calculated weekly during active life and closure period, monthly during post-closure care

## Slide 17: Surface Impoundments
Alternative Designs
  Must be at least as effective as composite liner system
  Must include a LDS
  GCL is common
Notes: Surface Impoundments
Alternative Designs
  Must be at least as effective as composite liner system
  Must include a LDS
  Geocomposite liner is most common
  Bentonite clay between fabric sheets

## Slide 18: Surface Impoundments
Monitoring and Inspection Requirements
  Weekly and after storms
    Freeboard (2’)
    Deterioration
    Malfunctions
    Severe Erosion
    Leaks
    Presence of Leachate in Sumps
Notes: Surface Impoundments
Monitoring and Inspection Requirements
  Weekly and after storms
    Freeboard (2’)
    Deterioration
    Malfunctions
    Severe Erosion
    Leaks
    Presence of Leachate in Sumps

## Slide 19: Surface Impoundments
Perimeter Dikes
  Structural Integrity Certified by P.E.
    Able to withstand pressure exerted by waste placement
    Will not fail due to scouring or piping
Notes: Surface Impoundments
Perimeter Dikes
  Structural Integrity Certified by P.E.
    Able to withstand pressure exerted by waste placement
    Will not fail due to scouring or piping
    piping is internal erosion by seepage

## Slide 20: Surface Impoundments
Closure
  Remove and decontaminate all waste and containment system components
  Unit may be closed as a Landfill if:
    Eliminate free liquids, stabilize remaining wastes (Meets LDR)
    Final cover surface impoundment
      Provide long term minimization of migration of liquids
      Function with minimum maintenance
      k less than or = k of bottom liner
Notes: Surface Impoundments
Closure
  Remove and decontaminate all waste and containment system components
  Unit may be closed as a Landfill if:
    Eliminate free liquids, stabilize remaining wastes (Meets LDR)
    Final cover surface impoundment
      Provide long term minimization of migration of liquids
      Function with minimum maintenance
      k less than or = k of bottom liner

## Slide 21: Surface Impoundments
Post-closure care
  For units closed as a Landfill
  Maintain Final Cover
  Maintain and monitor leak detection system
  Maintain groundwater monitoring system
Notes: Surface Impoundments
Post-closure care
  For units closed as a Landfill
  Maintain Final Cover
  Maintain and monitor leak detection system
  Maintain and monitor groundwater monitoring system

## Slide 22: Surface Impoundments
If Minimum Technology Requirements (MTR) not meet
  Facilities constructed prior to 1992
  Removal of Waste
  Decontamination of containment system components
  Contingency Plan to address waste left in place
    Final Cover System, groundwater monitoring
Notes: Surface Impoundments
If Minimum Technology Requirements MTR) not meet
  Facilities constructed prior to 1992
  Removal of Waste
  Decontamination of containment system components
  Contingency Plan to address waste left in place
    Final Cover System
    Groundwater monitoring

## Slide 23: Waste Piles
Design and Operating Requirements
  40 CFR Subpart L and 30 TAC 335.170
Liner system
  Top liner – (geomembrane)
  Composite bottom liner –
    Upper component – geomembrane
    Lower component – compacted clay liner
      3 feet thick
      k less than/equal to 10-7 cm/sec
Notes: Waste Piles
Design and Operating Requirements
  40 CFR Subpart L and 30 TAC 335.170
Liner system
  Top liner – (geomembrane)
  Leachate Collection System/Leak Detection system
    k is 10-2 cm/s and 12” thickness; or
    geonet where k is 10-5 cm/s or greater
THE INFORMATION FOR WASTE PILES IS HERE FOR REFERENCE IF TIME IS NEEDED.

## Slide 24: Waste Piles
Leachate Collection System/Leak Detection system
    k is 10-2 cm/s and 12” thickness; or
    geonet where k is 10-5 cm/s or greater
Notes: Waste Piles
Design and Operating Requirements
  40 CFR Subpart L and 30 TAC 335.170
Liner system
  Composite bottom liner –
    Upper component – geomembrane
    Lower component – compacted clay liner
      3 feet thick
      k less than/equal to 10-7 cm/sec

## Slide 25: Waste Piles
Closure
  Must remove waste
  Decontaminate all containment system components
  If contaminated soils can’t be removed, must close to landfill requirements
    Post-closure plan
Notes: Waste Piles
Closure
  Must remove waste
  Decontaminate all containment system components
  If contaminated soils can’t be removed (ie. Clean Closure), must close to landfill requirements
  Contingent post-closure plan

## Slide 26: Waste Piles In Texas
Approximately 6 initially permitted
All closed or undergoing closure
Notes: Waste Piles In Texas
Approximately 6 initially permitted
All closed or undergoing closure

## Slide 27: Land Treatment Units (LTU)
40 CFR 264 Subpart M and 30 TAC 335.171
Program to ensure
    Degradation;
    transformation or;
    immobilization
      Of all hazardous constituents
Notes: Land Treatment Units (LTU)
40 CFR 264 Subpart M and 30 TAC 335.171
A treatment program to ensure that hazardous constituents placed in or on the ground are degraded, transformed or immobilized within the treatment zone.

## Slide 28: LTU Treatment Program
Treatment demonstration
  Wastes that are capable of being treated
  Field tests, laboratory analysis, operating data
Operated in a manner to maximize degradation, transformation and immobilization
Unsaturated (Vadose) Zone Monitoring
Notes: LTU Treatment Program
Treatment demonstration
  Wastes that are capable of being treated
  Field tests, laboratory analysis, operating data
Operated in a manner to maximize degradation, transformation and immobilization
Unsaturated (Vadose) Zone Monitoring

## Slide 29: LTU Profile
Notes: Graphic of Typical Profile of Hazardous Waste Land Treatment Unit

## Slide 30: LTU Treatment Demonstration (LTD)
Field tests, laboratory analysis, operating data
Must simulate operating conditions
    Wastes
    Climate
    Topography
    Soil characteristics
    Operating practices
Notes: LTU Treatment Demonstration
Field tests, laboratory analysis, operating data
Must simulate operating conditions
    Wastes
    Climate
    Topography
    Soil characteristics
    Operating practices

## Slide 31: Land Treatment Units
Design and Operation Requirements
  Must continue to maximize degradation, transformation and immobilization of wastes
  Use same conditions as LTD
    Rate and Method of Waste Application
    Measures to control soil pH
    Measures to enhance microbial activity
    Measures to control moisture
Notes: Land Treatment Units
Design and Operation Requirements
  Must maximize degradation, transformation and immobilization of wastes
  Use same conditions as LTD
    Rate and Method of Waste Application
    Measures to control soil pH
    Measures to enhance microbial activity
    Measures to control moisture

## Slide 32: Land Treatment Unit
Design and Operation Requirements
  Maintain run-on control system from 25-year storm
  Manage run-off from 24-hour, 25-year event
  Inspect LTU weekly and after storms
    Deterioration
    Malfunctions
Notes: Land Treatment Units
Design and Operation Requirements
  Maintain run-on control system from 25-year storm
  Manage run-off from 24-hour, 25-year event
  Inspect LTU weekly and after storms
    Deterioration
    Malfunctions

## Slide 33: Land Treatment Units
Unsaturated Zone Monitoring
  Monitor soil and soil-pore liquid beneath treatment zone
    Obtain background soil core and soil-pore liquid concentrations
    Sample for principal hazardous constituents
    Site specific locations and frequency
      Statistical analysis allowed
Notes: Unsaturated Zone Monitoring
  Monitor soil and soil-pore liquid beneath treatment zone
    Sample for principal hazardous constituents (PHC)
    Obtain background soil core and soil-pore liquid concentrations
    Site specific locations and frequency
    Conduct statistical analysis

## Slide 34: Land Treatment Units
Closure
  Cease receipt of new waste
  Continue operation
    Maximum Degradation, Treatment, and Immobilization
  Maintain
    Aeration
    Moisture
    pH
    Nutrients
  Unsaturated Zone Monitoring
    Soil-pore monitoring may be terminated after 90 days
    If documented SSI – continue until no migration demonstrated
Notes: Closure
  Cease receipt of new waste
  Continuation of Operation other wise
    Goal is maximum degradation, treatment, and immobilization
  Maintain unit by:
    Continuing aeration
    Maintain appropriate moisture content
    Ensure proper pH
    Ensure adequate soil nutrients
  Unsaturated Zone Monitoring
    Soil-pore monitoring may be terminated after 90 days – from last application of waste unless an SSI is detected
    Continue soil core monitoring until PHC concentrations are below background.
    If documented SSI – continue until no migration demonstrated

## Slide 35: Land Treatment Units
Closure (cont.)
  Minimize run-off of hazardous constituents
  Maintain run-on/off control systems
  Continue Groundwater monitoring
Closure Activities
  180 day completion
    Longer period may be approved
    Period Dependent on :
      Waste loading rate at closure
      Waste degradation rate
    Typically can be completed in 90 to 360 days

## Slide 36: Land Treatment Units
Post-Closure Care
  Begins once Unsaturated Zone Monitoring Data shows equilibrium or background
  Active Management may continue
    Tilling
    Soil Amendments
    Vegetative Cover
  No post-closure release of hazardous constituents
Notes: Post-Closure Care
  Begins once Unsaturated Zone Monitoring Data shows equilibrium or background
  Active Management may continue
    Tilling
    Soil Amendments
    Vegetative Cover
  No post-closure release of hazardous constituents

## Slide 37: Land Treatment Units
Groundwater Monitoring during Post-Closure
  Required unless
    Hazardous Constituents do not exceed background
    No SSIs in Unsaturated Zone during active life
Releases
  PHCs migrated beyond treatment zone are above MCL or Background
    Removal of Contaminated Soil
    Placement of impermeable cap
    Continued management and monitoring
Notes: Groundwater Monitoring during Post-Closure
  Required unless
    Hazardous Constituents do not exceed background
    No SSIs in Unsaturated Zone during active life
Releases
  PHCs migrated beyond treatment zone are above MCL (Maximum Contaminant Level) or Background.
    Removal of Contaminated Soil
    (OR) Placement of impermeable cap
    Continued management and monitoring (Post Closure Care)

## Slide 38: Land Treatment Units in Texas
Approx. 24 Units are permitted in 1980s
  11 undergoing closure or post-closure care
  1 never constructed
Notes: Approx. 24 Units are permitted in 1980s
  11 undergoing closure or post-closure care
  1 never constructed

## Slide 39: Landfills
40 CFR 264 Subpart N
Design and Operating Requirements
  Liner System
    Top liner – i.e. geomembrane
    Leachate Collection System/Leak Detection System
      10-2 cm/sec and 1’ thickness or geonet with 10-5 cm/sec or greater
    Composite bottom liner –
      Upper component – geomembrane
      Lower component – compacted clay liner
        3 feet thick
        k less than/equal to 10-7 cm/sec
Notes: 40 CFR 264 Subpart N
Design and Operating Requirements
  Liner System
    Top liner – i.e. geomembrane
    Leachate Collection System/Leak Detection System
      10-2 cm/sec and 1’ thickness or geonet with 10-5 cm/sec or greater
    Composite bottom liner –
      Upper component – geomembrane
      Lower component – compacted clay liner
        3 feet thick
        k less than/equal to 10-7 cm/sec

## Slide 40: Landfills
Cover System
  Long-term minimization of liquid migration
  k less than or equal to that of the bottom liner system
Notes: Cover System
  Long-term minimization of liquid migration
  k less than or equal to that of the bottom liner system
Graphic of landfill cross-section
Graphic of landfill cell under construction

## Slide 41: Landfills
Alternative Designs
  Must be at least as effective as composite liner system
  Leak Detection
Operating Requirements
  Must prevent run-on from a 25-year storm
  Must contain a 24-hour, 25-year storm event
Notes: Alternative Designs
  Must be at least as effective as composite liner system
  Leak Detection
Operating Requirements
  Must prevent run-on from a 25-year storm
  Must contain a 24-hour, 25-year storm event

## Slide 42: Landfills
Action Leakage Rate (ALR)
  Maximum design flow rate that LDS can remove without the fluid head on the bottom liner exceeding thickness of drainage media.
    Average daily flow rate for each sump (calculated as gallons per acre per day)
    Calculated weekly during active life and closure period, monthly during post-closure care
Notes: Action Leakage Rate (ALR)
  Maximum design flow rate that LDS can remove without the fluid head on the bottom liner exceeding thickness of drainage media.
  Average daily flow rate for each sump (calculated as gallons per acre per day)
  Calculated weekly during active life and closure period, monthly during post-closure care

## Slide 43: Landfills
Response Action Plan (RAP) – if flow rate exceeds ALR
  Notify TCEQ within 7 days
  Submit assessment report within 14 days
  Determine if waste receipt should cease
  Within 30 days, report your action taken and action planned
Notes: Response Action Plan (RAP) – if flow rate exceeds ALR
  Notify TCEQ within 7 days
  Submit assessment report within 14 days
  Determine if waste receipt should cease
  Within 30 days, report your action taken and action planned

## Slide 44: Landfills
Closure
  Final cover system
    Provide long term minimization of migration of liquids
    Function with minimum maintenance
    Promote drainage and minimize erosion
    Accommodate settling and subsidence
    k less than k of bottom liner
  Components (Bottom to Top)
    3ft of compacted clay with k of 10-7 cm/sec or less.
    Geomembrane
    Drainage Layer
    Soil capable of sustaining native plant growth
Notes: Closure
  Final cover system
    Provide long term minimization of migration of liquids
    Function with minimum maintenance
    Promote drainage and minimize erosion
    Accommodate settling and subsidence
    k less than k of bottom liner
  Components (Bottom to Top)
    3ft of compacted clay with k of 10-7 cm/sec or less.
    Geomembrane
    Drainage Layer
    Soil capable of sustaining native plant growth

## Slide 45: Landfills
Post-closure care
  Maintain final cover
  Continue to operate
    leachate collection system
    leak detection system
  Continue GW monitoring
  Prevent run-on and run-off from storm events damaging cover system
Notes: Post-closure care
  Maintain final cover
  Continue to operate
    leachate collection system
    leak detection system
  Continue GW monitoring
  Prevent run-on and run-off from storm events damaging cover system

## Slide 46: Corrective Action Management Units (CAMU)
  40 CFR 264, Subpart S – Special Provisions for Cleanup
  Special Unit for the disposal of waste from on-site clean up.
  Implemented to remove the disincentives to clean-up
Notes:   40 CFR 264, Subpart S – Special Provisions for Cleanup
  Special Unit for the disposal of waste from on-site clean up.
  Implemented to remove the disincentives to clean-up

## Slide 47: Corrective Action Management Units (CAMU)
Design Standards
  Composite Liner
  2 foot thick clay with k =10-7 cm/sec
  FML = 30-mil or HDPE = 60-mil
  Leachate Collection System
    Maintain less than 1’ of leachate over liner
Alternative Designs
  Must be at least as effective as proscribed liner system
  Leachate Collection System
Notes: Design Standards
  Composite Liner
  2 foot thick clay with k =10-7 cm/sec
  FML = 30-mil or HDPE = 60-mil
  (Flexible Membrane Liner)
  Leachate Collection System
    Maintain less than 1’ of leachate over liner
Alternative Designs
  Must be at least as effective as proscribed liner system
  Leachate Collection System

## Slide 48: Corrective Action Management Units (CAMU)
Closure
  Final cover system
    Provide long term minimization of migration of liquids
    Function with minimum maintenance
    Promote drainage and minimize erosion
    Accommodate settling and subsidence
    k less than k of bottom liner
  Groundwater Monitoring Required
    Existing/Suspected releases to from within CAMU
    Wastes will remain in place after closure of the CAMU
Notes: Closure
  Final cover system
    Provide long term minimization of migration of liquids
    Function with minimum maintenance
    Promote drainage and minimize erosion
    Accommodate settling and subsidence
    k less than k of bottom liner
  Groundwater Monitoring Required
    Existing/Suspected releases to from within CAMU
    Wastes will remain in place after closure of the CAMU

## Slide 49: Sign Up for GovDelivery
Receive the I&HW Quarterly update, and notification of IHW forms, rule, guidance, and procedure updates:
http://www.tceq.texas.gov/permitting/ waste_permits/ihw_permits/signupihw
[Pictures of the first and second pages of the Spring 2017 I&HW Quarterly Highlights.]
Notes: Sign Up for GovDelivery
Receive the I&HW Quarterly update, and notification of IHW forms, rule, guidance, and procedure updates:
http://www.tceq.texas.gov/permitting/waste_permits/ihw_permits/signupihw
[Pictures of the first and second pages of the Spring 2017 I&HW Quarterly Highlights.]
There is possibility for adding subgroups to the listserv (for example, rulemaking or combustion groups).

## Slide 50: Useful Agency Links:
TCEQ Home Page: http://www.tceq.texas.gov/
Has links to 30 TAC Rules and Federal sites
IHW Permitting Home Page: https://www.tceq.texas.gov/permitting/ waste_permits/ihw_permits/ihw.html

## Slide 51: More Information?
Contact the I&HW Permits Section at
(512) 239-2335
or
ihwper@tceq.texas.gov

## Slide 52: Questions
Charles Brown, P.G.
(512)239-6234
Charles.Brown@tceq.texas.gov
Michael Pimentel, P.E.
(512)239-6409
Michael.Pimentel@tceq.texas.gov