## Slide 1: How Title V and NSR Permitting Interact
Ariel Ramirez
NSR, Air Permits Division
Vasant Chaphekar, P.E.
Title V, Air Permits Division
2019 Environmental Trade Fair and Conference
Notes: How Title V and NSR Permitting Interact
Ariel Ramirez
Air Permits Division
Texas Commission on Environmental Quality
Environmental Trade Fair 2019
Vasant Chaphekar, P.E.
Air Permits Division
Texas Commission on Environmental Quality
Environmental Trade Fair 2019
The purpose of this presentation is to discuss the relationship between New Source Review (NSR) and Title V Permits and how they interact.
Image Attribution: https://tpwd.texas.gov/newsletters/eye-on-nature/2015fall/page2.phtml
Good afternoon, my name is Ariel Ramirez. My colleague Vasant Chaphekar and I will be talking to you today about Title V and New Source Review permitting and how they relate to each other. Before we get started, I’d like to point out that a copy of this presentation is posted on the TCEQ website. This document includes acronyms and abbreviations that are used throughout the presentation. I would also like to mention that this presentation includes content that was covered during the Title V and NSR presentations given earlier during this Trade Fair, so our presentation assumes you have a basic understanding of Title V and NSR permits. [NEXT]

## Slide 2: Presentation Outline
Summary
Examples
Interaction
NSR
FOP
Comparison
NSR
FOP
The Texas 2-Step
Introduction
Notes: Presentation Outline
Introduction
The Texas 2-Step
Comparison
Interaction
Examples
Summary
Image Attributions:
Texas created by Leonardo Schneider, US, from The Noun Project, thenounproject.com
After a brief introduction of the air permitting timeline in Texas, we will discuss the “Texas 2-step” permitting system. [NEXT] We will then show a comparison of how Title V, also called a Federal Operating Permit (or FOP), and NSR permits differ and interact. I would like to mention that Title V and FOP will be used interchangeably throughout this presentation, so please keep in mind that this is referring to the same permit. [NEXT] Finally, we will conclude our presentation with multiple examples to help summarize what we have covered here today. [NEXT]

## Slide 3: Air Permitting Timeline in Texas
1990-Amend.
FCAA
1977-Amend.
FCAA
1971-Amend.
TCAA
1970
FCAA
1965
TCAA
Air Permitting Timeline in Texas
Notes: Brief History
Federal Clean Air Act (FCAA) and the Texas Clean Air Act (TCAA)
TCAA 1965 – Texas Clean Air Act first passed in 1965 and the Texas Air Control Board (TACB) was created within the Department of Health.
FCAA 1970 – FCAA of 1970 established the major framework that is still in use today. The National Environmental Policy Act (NEPA) in 1970 led to the EPA.
TCAA 1971 – Amendments in 1971 established authority for the air permits program.
FCAA 1977 – Congress established the NSR permitting program as part of the 1977 Federal Clean Air Act Amendments. These amendments codified requirements for review of major permitting actions (PSD and Nonattainment).
FCAA 1990 – Congress passed the FCAA Amendments of 1990, which included the new provisions in Title V, creating an operating program to ensure better compliance and allow for more thorough air pollution control.
Links:
30 TAC Chapter 101, Subchapter H: http://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=5&ti=30&pt=1&ch=101&sch=H
Division 1: http://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=5&ti=30&pt=1&ch=101&sch=H&div=1&rl=Y
Division 4: http://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=5&ti=30&pt=1&ch=101&sch=H&div=4&rl=Y
First off, let’s review a brief history to show how the Federal Clean Air Act (FCAA) and the Texas Clean Air Act (TCAA) helped shape air permitting in Texas
The Texas Clean Air Act first passed in 1965. At this time, the Texas Air Control Board was created within the Department of Health. [NEXT] The Federal Clean Air Act of 1970 established the major framework that is still in use today. The National Environmental Policy Act (NEPA) in 1970 led to the creation of the EPA, [NEXT] and amendments in 1971 established authority for the air permits program. [NEXT] Congress the established the NSR permitting program as part of the 1977 Federal Clean Air Act Amendments. These amendments codified requirements for review of major permitting actions (PSD and Nonattainment). [NEXT] Later on, congress passed the Federal Clean Air Act Amendments of 1990, which included the new provisions in Title V. This created an operating program to ensure better compliance and allow for more thorough air pollution control. [NEXT]

## Slide 4: AIR PERMITTING
* FOP is required for all major sources and some non-major sources
Step 2: Operating Permit*
Title V or Federal Operating Permit (FOP)
30 TAC §122
Step 1: Construction Permit
New Source Review (NSR)
30 TAC §106 and §116
The Texas 2-Step Permitting System
Notes: Air Permitting
Step 1: Construction Permit - “New Source Review (NSR)”
  30 TAC Chapters 106 and 116
Step 2: Operating Permit – “Title V” or “Federal Operating Permit (FOP)”
  30 TAC Chapter 122
Step 2 is conditional, since not all sites that have an NSR permit are subject to FOP requirements. FOP is required for all major sources and some non-major sources that are listed by EPA under 40 CFR Part 70.3(a).
Links:
30 TAC Chapter 106: https://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=4&ti=30&pt=1&ch=106
30 TAC Chapter 116: https://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=4&ti=30&pt=1&ch=116
30 TAC Chapter 122: https://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=4&ti=30&pt=1&ch=122
The “Texas 2-Step” Permitting System includes the following steps:
In Step 1, a construction (or NSR) permit is obtained. NSR permits are authorizations required to construct a new facility or modify an existing facility. Requirements for NSR permits can be found in 30 TAC §106 and §116. [NEXT]
In Step 2, if required, an operating Permit (Title V or FOP) is obtained. This is a legally enforceable document required for all major sources and some non-major sources. It is important to note that not all sources that have a NSR permit will be subject to a FOP. Requirements for the FOP program are stated in 40 CFR Part 70, as well as 30 TAC §122. [NEXT]

## Slide 5: NSR
Authorizes facilities prior to construction
Establishes maximum allowable emission rates
Evaluates health impacts
Conducts BACT review
Evaluates federal applicability
FOP
Comparison
New Source Review (NSR)
Notes: NSR
Authorizes facilities prior to construction/modifications. Permit can be issued independently. NSR can be incorporated by reference into the FOP. Note that this is not the other way around (i.e., FOP is not incorporated by reference into the NSR. The NSR permit must be obtained before any actual work begins at/on the facility.
Authorizes facilities that may emit air contaminants and establishes the maximum allowable emission rates for each point source. These rates are included in the Maximum Allowable Emission Rate Table (MAERT).
Evaluates heath impacts for all proposed emissions increase, as well as any proposed new air contaminants. Impacts must be deemed acceptable before the NSR permit can be issued.
Conducts a Best Available Control Technology (BACT) review which applies to all sources that are newly proposed or being modified. BACT review is also required for all sources that are being incorporated by consolidation via PBR or SP.
Evaluates federal applicability (PSD/NA)
Image Attribution:
Texas created by Leonardo Schneider, US, from The Noun Project, thenounproject.com
NSR permits authorize facilities prior to construction or modification, can be issued independently, and must be obtained before any actual work begins at or on the facility. The NSR permit can be incorporated by reference into the Title V, which we will be discussing in more detail later. It is important to note that this is not the other way around. In other words, Title V is not incorporated by reference into the NSR. [NEXT]
NSR permits authorize facilities that may emit air contaminants and establishes the maximum allowable emission rates for each point source. These rates are included in the Maximum Allowable Emission Rate Table (MAERT). [NEXT] NSR permits also evaluate heath impacts for all proposed emissions increases, as well impacts for any proposed new air contaminants. The impacts must be deemed acceptable before the NSR permit can be issued. [NEXT] NSR permits include a Best Available Control Technology (or BACT) review which applies to all sources that are newly proposed or being modified. A BACT and impacts review is also required for all sources that are being incorporated by consolidation via Permit by Rule or Standard Permit. [NEXT] NSR also evaluates federal applicability, which includes Prevention of Significant Deterioration (or PSD) and Nonattainment (NA) review. [NEXT]

## Slide 6: Permitting Options
Comparison
FOP
Emission Increase
De Minimis
§116.119
PBR
§106
Standard Permit
§116.601
NSR Permit
§116
NSR
Notes: NSR Permitting Options
Before any actual work begins, any person who plans to construct any new facility or to engage in the modification of any existing facility which may emit air contaminants into the air must: (Note that the term “facility” in Chapter 116 is the same as “emission unit” in Chapter 122).
Satisfy the criteria for a de minimis facility or source;
Satisfy the conditions of a permit by rule (PBR);
Satisfy the conditions of a standard permit; or
If the above authorization mechanisms cannot be used, obtain an NSR permit.
In addition to new construction and modification to existing facilities, other activities requiring NSR authorization include changes in application representations and renewal of existing authorizations.
Some facilities and sources are classified as de minimis and authorized by rule. 30 TAC §116.119 identifies criteria for determining de minimis classifications. In addition, specific facilities that have been evaluated and designated as de minimis are identified on the de minimis list, which is posted on the division's Web site. De minimis facilities and sources include very small additions to background concentrations of air contaminants that cause no discernable or unacceptable impact to public health and for which permitting would be an ineffective use of commission resources. Some examples of de minimis sources are music and film studios, beauty shops, and deer block manufacturing. This authorization is intended to reduce workload and allow permitting staff to focus on projects that could affect public health and welfare. Applicants with facilities that meet the de minimis rule or de minimis list do not have to obtain an air authorization through the permitting process. All emissions associated with the facility, or any group of facilities, must meet the de minimis criteria. No partial permitting allowed!
Facilities with emissions that do not meet de minimis criteria but will not make a significant contribution of air contaminants to the atmosphere may be permitted by rule. Facilities that are permitted by rule include less complex comfort heating facilities to more complex facilities and activities such as those found at oil and gas sites. The commission has adopted permits by rule (PBRs) in 30 Texas Administrative Code Chapter 106. Subchapter A of Chapter 106 contains general requirements applicable to all PBRs, including (but not limited to) recordkeeping and emission limitations. In addition to the general requirements that are contained in Subchapter A, many individual PBRs also contain conditions specific to that PBR that must be met. When a PBR is claimed, applicable requirements of both the PBR and Subchapter A must be met. It should also be noted that some PBRs require registration and others do not.
A standard permit authorizes the construction or modification of new or existing facilities that are similar in terms of operations, processes, and emissions. A standard permit provides an efficient mechanism for qualifying facilities to obtain authorization as an alternative to a case-specific air quality permit. If a facility cannot meet a PBR, then the applicant should see if a standard permit can be claimed. A standard permit can never be used to authorize emissions that will trigger major NSR permitting under Chapter 116. Standard permit registrations must be renewed every ten years. In addition, if the executive director amends a standard permit, the facility must comply with the amended standard permit. Compliance is usually required by the renewal date of the standard permit registration but cannot be required within 24 months of the standard permit amendment, unless it is necessary to protect public health.
If a facility is not de minimis and cannot meet a PBR or standard permit, it must be authorized by a case-by-case NSR permit. These types of authorizations provide more flexibility to applicants because they can authorize more emissions and, unlike a PBR or standard permit, facility-specific information can be considered during the technical review, which includes a BACT and impacts review. NSR permits are subject to public notice and an opportunity for a contested case hearing. These permits are issued with a ten-year renewal cycle. Renewals MAY require NSR authorizations; note that renewals are NOT required for PBRs.
Links:
30 TAC §116.119: https://texreg.sos.state.tx.us/public/readtac$ext.TacPage?sl=R&app=9&p_dir=&p_rloc=&p_tloc=&p_ploc=&pg=1&ti=30&ch=116&rl=119
30 TAC §106: https://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=4&ti=30&pt=1&ch=106
30 TAC §116.601: https://texreg.sos.state.tx.us/public/readtac$ext.TacPage?sl=R&app=9&p_dir=&p_rloc=&p_tloc=&p_ploc=&pg=1&p_tac=&ti=30&pt=1&ch=116&rl=601
30 TAC §116: https://texreg.sos.state.tx.us/public/readtac$ext.ViewTAC?tac_view=4&ti=30&pt=1&ch=116
Before any actual work begins, any person who plans to construct a new facility, or engage in the modification of an existing facility which may emit air contaminants, must satisfy the criteria for either: [NEXT] a de minimis facility or source; [NEXT] a Permit by Rule; [NEXT] a Standard Permit; [NEXT] or if those authorization mechanisms cannot be used, obtain a case-by-case NSR permit. Additionally, other activities that require NSR authorization include changes in application representations, as well as the renewal of existing authorizations. [NEXT]

## Slide 7: What does a NSR Permit Contain?
FOP
Comparison
MAERT
Attachments
Special Conditions
Permit Face with General Conditions
NSR
Notes: What does a NSR Permit Contain?
Permit Face with General Conditions
  Name of company, location of facilities authorized, permit number, issuance date, permit renewal date, signature of Executive Director, General Conditions.
Special Conditions
  Enforceable operating conditions with which the applicant must comply, ensure compliance with representations, developed through negotiation with permit applicant, “boilerplate” language is used as a starting point, may have attachments.
  Special Conditions contain conditions with monitoring and recordkeeping requirements that are used to demonstrate compliance with the emission rates on the MAERT.
Attachments to the Special Conditions (if applicable)
Maximum Allowable Emission Rates Table (MAERT)
  Emission point number (EPN), name of emission point (source name, maximum allowable emission rate for each pollutant in maximum pounds per hour and tons per year.
So what does the NSR Permit contain? First off, it contains the Permit Face which includes the name of the company, the location of the facilities authorized, permit number, issuance date, permit renewal date, signature of the Executive Director, and General Conditions. [NEXT]
The permit also includes Special Conditions and any applicable attachments to the conditions. The Special Conditions are enforceable operating conditions with which the applicant must comply to ensure compliance with their submitted permit representations. The condition language is developed using “boilerplate” language as a starting point, and is finalized through negotiation with permit applicant. The Special Conditions contain monitoring and recordkeeping requirements that are used to demonstrate compliance with the emission rates on the MAERT. [NEXT]
The MAERT, or Maximum Allowable Emission Rates Table, contains the emission point numbers of each authorized source, the names of emission points (or source names), and the maximum allowable emission rate for each pollutant in maximum pounds per hour and tons per year. [NEXT]

## Slide 8: Federal Operating Permit (FOP)
FOP
Codifies previously authorized air emissions
Documents Applicable Requirements
  Regulations and Monitoring/Testing, Reporting & Recordkeeping (MRRT)
  May add Periodic Monitoring (PM) and Compliance Assurance Monitoring (CAM) if required
Requires annual compliance certification
Comparison
NSR
Notes: So, an NSR permit is required for new and modified facilities. Title V is an air permitting program generally specific to major sources. All air emissions are authorized by an NSR permit. A Title V permit codifies previously authorized air emissions and documents all applicable requirements in a single document. Title V does not authorize any air emissions. Applicable requirements include listing all applicable regulations and Monitoring/Testing, Reporting & Recordkeeping (MRRT) requirements under state and federal rules. In addition, Title V permit can also add Periodic Monitoring (PM) and Compliance Assurance Monitoring (CAM) if required. The Title V permit requires the site to submit an annual compliance certification.
The term “major source” refers to the entire site. Any site that emits, or has the potential to emit, any of the following is a major source; and therefore, must obtain a Title V operating permit:
Ten tons per year or more of any single hazardous air pollutant (HAP) or 25 tons per year or more of any combination of HAPs; or
100 tons per year or more of any regulated air pollutant. If the site is located in a serious, severe, or extreme nonattainment area, the thresholds would be less than 100 tons per year of the appropriate criteria pollutant or precursor.
Title V applies to certain non-major sources as well that are listed by EPA under 40 CFR Part 70.3(a). Details can be found at: https://www.tceq.texas.gov/assets/public/permitting/air/Guidance/Title_V/non_major.pdf
A Federal Operating Permit codifies previously authorized air emissions and documents applicable requirements. [NEXT] Applicable requirements include Monitoring, Testing, Reporting, and Recordkeeping (or MRRT). In addition, Periodic Monitoring (PM), and Compliance Assurance Monitoring (CAM) are added if required. [NEXT] The FOP also requires annual permit compliance certification and bi-annual deviation reporting.
While a NSR permit is required for new and modified facilities, a FOP is applicable to major sources and some non-major sources. The non-major sources are listed by the EPA under 40 CFR Part 70.3(a)), and the term “major source” refers to the entire site as defined in 30 TAC Chapter 122.
Any site that emits, or has the potential to emit, any of the following is defined as a major source; and therefore, must obtain a Title V operating permit: This would be
- (1)…10 tpy or more of any single hazardous air pollutant (HAP); or 25 tpy or more of any combination of HAPs; or
- (2)…100 tpy or more of any regulated air pollutant. If the site is located in a serious, severe, or extreme nonattainment area, the thresholds would be less than 100 tpy of the appropriate criteria pollutant or precursor. [NEXT]

## Slide 9: What Does a Title V SOP Contain?
FOP
Comparison
Appendices
Attachments
Terms and Conditions
Table of Contents
Permit Face
NSR
Notes: Site operating permits (SOPs) are Title V permits that contain requirements specific to an individual site and thus, receive case-by-case reviews. The permits contain requirements that apply to the site as a whole, as well as requirements that are specific to individual emission units. All Title V SOPs are subject to public notice or public announcement requirements and public may request a public comment hearing. With the public notice there is an affected state review (if the site is within 50 miles of an affected state),and a 45-day Environmental Protection Agency (EPA) review. After SOP is issued there is a public petition (which is a 60-day period after SOP issuance). SOPs must be renewed at least every five years.
SOP Attachments include:
Applicable Requirements Summary
Additional Monitoring Requirements (CAM/PM)
Permit Shield
NSR Authorization References
Compliance Schedule
Alternative Requirement
SOP Appendices include:
Acronym List
Major NSR Summary Table and NSR Permit(s)
Now we will take a look at what a Title V Standard Operating Permit, (which is a type of site-specific FOP) contains:
There’s a permit face, [NEXT] table of contents, [NEXT] terms and conditions, [NEXT] attachments, [NEXT] and appendices. Attachments include:
  An Applicable Requirements Summary table;
  Additional Monitoring Requirements (CAM/PM);
  List of Permit Shields, if requested;
  A NSR Authorization References table;
  A Compliance Schedule, if required;
  and Alternative Requirements, if applicable.
The Appendices include an acronym list, and if required, a Major NSR Summary Table and a copy of the NSR Permit(s). [NEXT]

## Slide 10: Permit Feature Comparison of FOP and NSR
FOP
Comparison
Permit Feature | FOP | NSR
* NSR permit referenced in FOP must be issued first
# Codifies existing applicable requirements but can add PM/CAM
No
Yes
Annual permit compliance certification report?
Yes
No
Allows contested case hearings?
No
Yes
Is one permit referenced in another?
Yes
Yes*
Issued independently?
Yes
No#
Can impose additional requirements on sources?
Yes
No
Applies to all point source emissions in TX?
Up to 2
1
Public notice requirements
Yes
No
Evaluates health effects and BACT?
Yes
No
Authorizes construction and air emissions?
NSR
Notes: Regarding “#” footnote: ‘No’ is a qualified “No” since periodic monitoring (PM) or CAM requirements may be added for emission units above and beyond what is required in the state or federal regulations if these regulations lack sufficient monitoring for demonstrating compliance.
Regarding “*” footnote: NSR permits that are referenced in the FOP must be issued first before they can be incorporated by reference in the FOP.
Now we will go through a table which compares multiple permit features of FOP and NSR permits:
Does the permit authorize construction and air emissions? [NEXT]
Does the permit evaluate for health effects and BACT? [NEXT]
Does the permit require public notice? [NEXT]
Does the permit apply to all point source emissions in Texas? [NEXT]
Can the permit impose additional requirements on the sources? [NEXT]
  Regarding the “#” footnote: ‘No’ is a qualified “No”. If regulations lack sufficient monitoring for demonstrating compliance, Periodic Monitoring or Compliance Assurance Monitoring requirements may be added for emission units above and beyond what is required in the state or federal regulations.
Can the permit be issued independently? [NEXT]
  Regarding “*” footnote: NSR permits that are referenced in the FOP must be issued first before they can be incorporated by reference into the FOP. [NEXT]
Does the permit allow for contested case hearings? [NEXT]
And finally, does the permit require the permit holder to submit an annual permit compliance certification report? [NEXT]

## Slide 11: Example: Major Source Threshold Levels
Emission Source | FOP | NSR
* Source not listed in 30 TAC §122.10(13)(C) or 30 TAC § 116.164(a)(1)
Un-named* Source
PTE ≥ 100 but < 250 tpy in Attainment Area
Un-named Source
PTE ≥ 250 tpy in Attainment Area
Any Source PTE ≥ Threshold for NA Area Designation
Major
Minor
Major
Major
Major
Major
Notes: An unnamed source is a source that is not listed in 30 TAC 122.10(13)(C) or 30 TAC 116.164(a)(1). Note in this table a source may not be classified as a major for NSR review purpose but site is a major for FOP review purpose. So, what is the difference between a “site” and a “source” – for TV purposes? A site is defined in 30 TAC 122.10(27). The site may include one or more stationary sources that meet certain qualification criteria stated in the definition. Definition of a “major” source for NSR purpose is found in 40 CFR 70.2, as well as the PSD rules in 40 CFR 51.165. Under NSR permitting, named sources are major at 100 tpy per 30 TAC 116.12(19) and the referenced 40 Code of Federal Regulations (CFR) §51.166(b)(1).
Note that units authorized by NSR but not yet constructed are not required to be included in the PTE calculation.
Here we have an example to compare Major Source Threshold Levels for a FOP and NSR permits. In the first case we have
an un-named Source with a Potential to Emit (or PTE) greater than 100 tpy, but less than 250 tpy, in an attainment area. [NEXT]
Next we compare another un-named source with a PTE greater than 250 tpy in an attainment area. [NEXT]
and finally, we compare any source which has a PTE greater than the threshold for it’s respective nonattainment area designation.
The footnote shows that an ‘unnamed source’ is a source that is not listed in 30 TAC §122.10(13)(C) or §116.164(a)(1). An important takeaway from this slide is that the same source may be classified as minor for NSR review, but as major for FOP review. Also note that units authorized by NSR, but not yet constructed, are not required to be included in the PTE calculation. [NEXT]

## Slide 12: Interaction
Per §122.10(2), Applicable Requirements in a FOP include applicable NSR and PBR permits.
The NSR and PBR permits are incorporated by reference (IBR) in the FOP to facilitate compliance and enforceability.
Examples
Summary
Notes: Per 30 TAC Chapter 122, Applicable Requirements in a FOP include all NSR and PBR permits for the permitted sources. Although incorporation by reference (IBR) is not defined as a term in Chapter 122, 122.142 (b)(3) indicates “Each permit for which the executive director has not authorized initiation of public notice by June 3, 2001 shall contain any preconstruction authorization that is applicable to emission units at the site.” All NSR and PBR permits for the permitted sources are incorporated by reference (IBR) in a FOP for documentation purpose and to facilitate compliance and enforceability.
Image Attribution:
Texas created by Leonardo Schneider, US, from The Noun Project, https://thenounproject.com/term/texas/97870/
Now, let’s take a look at how FOP and NSR interact.
Per §122, Applicable Requirements in a FOP include all NSR and PBR permits for the permitted sources.
Although incorporation by reference is not defined as a term in Chapter §122…subpart 142(b)(3) states “Each permit for which the executive director has not authorized initiation of public notice by June 3, 2001 shall contain any preconstruction authorization that is applicable to emission units at the site.” [NEXT]
As such, all NSR and PBR permits for the permitted sources are incorporated by reference (IBR) in a Federal Operating Permit for documentation purposes, and to facilitate compliance and enforceability. [NEXT]

## Slide 13: Interaction: PSD and NA
Examples
Summary
If a major NSR site has a PSD/NA permit, then FOP must include:
  Major NSR Summary Table; and
  Copy of the PSD/NA NSR permit.
Interaction
Notes: If a site is Major for NSR and has a PSD/NA permit, FOP includes a Major NSR Summary Table and a copy of the PSD/NA NSR permit that is incorporated by reference (IBR).
Image Attribution:
Texas created by Leonardo Schneider, US, from The Noun Project, https://thenounproject.com/term/texas/97870/
If a site is Major for NSR and has a PSD or Nonattainment permit, the FOP must include a Major NSR Summary Table as well as a copy of the PSD/NA NSR permit that is incorporated by reference (IBR). [NEXT]

## Slide 14: Example: New Source Review Authorization References in FOP
Prevention of Significant Deterioration (PSD) Permits | 
PSD Permit No.: PSDTX9999 | Issuance Date: 05/01/2010
Title 30 TAC 116 Permits, Special Permits, and other Authorizations | 
Authorization No.: 99999 | Issuance Date: 05/01/2010
Permits By Rule (30 TAC Chapter 106) for the Application Area | 
Number: 106.261 | Version No./Date: 11/01/2003
Number: 106.262 | Version No./Date: 11/01/2003
Notes: Example: New Source Review Authorization References
Shown here is a copy of a page in the FOP permit which references all NSR permits for all units included in the FOP.
Shown here as an example is a page in the Federal Operating Permit which references NSR permits for units that are included within the FOP.
Note that this lists PSD/NA permits issued under Title I; NSR, Special Permits, and other Authorizations issued under Chapter 116; and PBRs issued under Chapter 106. This page also lists all of the respective issuance dates or effective dates for each of these permits or registrations, respectively. [NEXT]

## Slide 15: Example: New Source Review Authorization References by Emission Unit in FOP
Unit/Group/Process ID | EU Name/Descriptor | NSR Authorization
BOIL-1 | Boiler House 1 | 99999/PSDTX9999
ENGINE-1 | Pump Engine | 106.511/09/04/2000
Example:
New Source Review Authorization References by Emission Unit in FOP
Notes: Example: NSR Authorization References by Emission Unit
This slide shows how New Source Review Authorization References by Emission Unit are listed in the FOP.
Shown here is an example of how NSR Authorization References by Emission Unit are listed in the FOP. As you can see, the Unit/group/process ID is listed along with a descriptor, and followed by the specific NSR authorization that the unit is authorized under. Each emission unit/source in the FOP must be authorized by an NSR permit issued under Chapter 116, or a PBR issued under Chapter 106.[NEXT]

## Slide 16: Title V and what is incorporated
Examples
Summary
NSR#*
SP#*
PBR#*
NSPS*
MACT*
SIP*
PM/CAM*
NESHAPS*
Title V Permit
* Applicable Requirements
# Incorporated by Reference
Interaction
Notes: In this slide FOP is depicted as a jig-saw puzzle that has multiple components that can work independently but are integrated into a single cohesive permit that documents all applicable requirements for a site. As described earlier, a FOP includes an applicable requirements summary (ARS) table. ARS lists all units that are subject to a regulation and specifically documents all applicable state and federal citations such as SIP, NSPS, NESHAPS and MACT for each operating index and pollutant. ARS also documents MRRT including PM/CAM for each unit. All NSR permits like PBRs, SPs and case-by-case NSR permits are incorporated by reference (IBR) as shown on the earlier slide.
Image Attributes:
Puzzle image can be found at https://thenounproject.com/andydoane/collection/puzzle-pieces/?i=1445716.
Missing Puzzle Piece by Andrew Doane.
Puzzle piece image can be found at https://thenounproject.com/andydoane/collection/puzzle-pieces/?i=663744.
Puzzle Piece by Andrew Doane.
In this slide, the Title V permit is depicted as a jigsaw puzzle that has multiple components. These components can work independently, but are integrated into a single cohesive permit framework that documents all applicable requirements for a major source.
As mentioned earlier, Title V includes an applicable requirements summary (or ARS) table. The ARS lists all units that are subject to a regulation and specifically documents all applicable state and federal citations for each operating index and pollutant. These include state implementation plans (SIP), NSPS, NESHAPS and MACT. The ARS also documents MRRT, which includes PM and CAM as required for each unit.
All NSR Permits (shown here as single puzzle pieces for PBRs, Standard Permits, and case-by-case NSR permits) are incorporated by reference in the Title V permit.[NEXT]

## Slide 17: Title V and what is incorporated, continued
Examples
Summary
NSR#*
SP#*
PBR#*
NSPS*
MACT*
SIP*
PM/CAM*
NESHAPS*
Title V Permit
* Applicable Requirements
# Incorporated by Reference
PBR#*
SP#*
NSR#*
NSPS*
MACT*
SIP*
PM/CAM*
NESHAPS*
Interaction
Notes: A solved jigsaw puzzle illustrates the fact that FOP is an all-inclusive single operating permit that consolidates all applicable state and federal regulations including all NSR permits into one document.
Image Attributes:
Puzzle image can be found at https://thenounproject.com/andydoane/collection/puzzle-pieces/?i=1445716.
Missing Puzzle Piece by Andrew Doane.
Puzzle piece image can be found at https://thenounproject.com/andydoane/collection/puzzle-pieces/?i=663744.
Puzzle Piece by Andrew Doane.
Now we see the Title V permit represented as a solved jigsaw puzzle. This illustrates the fact that Title V is an all-inclusive single federal operating permit, which consolidates all applicable state and federal regulations for a major source, into a single document. As is illustrated here and also in the next slide, all NSR permits that authorize the major source become a part of a Title V permit because they are incorporated by reference. [NEXT]

## Slide 18: MRRT requirements
Examples
Summary
MRRT type requirements under Title V may also be included in NSR permits
PM
CAM
TESTING
REPORTING
RECORDKEEPING
Interaction
Notes: NSR requirements that are similar to the requirements found in the FOP may include, Monitoring, Testing, Reporting, and Recordkeeping (MRRT). MRRT may also include adding CAM and PM monitoring to demonstrate compliance with the special terms and MAERT limits listed in the NSR permit and the NSR requirements may be different from similar requirements codified in the FOP for other (non-NSR) applicable requirements.
Image Attributes
Puzzle image can be found at https://thenounproject.com/andydoane/collection/puzzle-pieces/?i=1445716.
Missing Puzzle Piece by Andrew Doane.
NSR requirements that are similar to the requirements found in the FOP may include Monitoring, Testing, Reporting, and Recordkeeping (or MRRT). MRRT may also include adding CAM and PM requirements which are used to demonstrate compliance with the Special Conditions, as well as the MAERT limits listed in the NSR permit. Note that the NSR requirements may be different from similar requirements codified in the Title V for other (non-NSR) applicable requirements. [NEXT]

## Slide 19: NSR Workbook and Title V
PM/CAM
Monitoring/
Testing
Recordkeeping/
Reporting
The NSR permit application workbook includes MRRT…
Notes: As you may be aware that starting in June 1, 2019, all case-by-case NSR permit applications must include a workbook. The NSR permit application workbook has built-in features and includes checks and balances that will identify MRRT type requirements that may be required in your permit to demonstrate compliance with the special terms and MAERT limits listed in the NSR permit.
NSR requirements that are similar to the requirements found in the FOP include monitoring, testing, reporting, recordkeeping, PM, and CAM requirements. These requirements are detailed within the NSR permit application workbook and helps to ensure that all of the requirements are addressed.
Why CAM and PM? CAM and PM may be added to some NSR permits if the permit has insufficient (or no) monitoring, recordkeeping, reporting, or testing to assure compliance with standards and proper operation of the control devices, including work practice standards, emission limitations, control requirements, and representations in application. Important aspects of monitoring include parameters, frequency, averaging time, deviation threshold, QA/QC, and recordkeeping. CAM and PM that may be added to demonstrate compliance with NSR permit requirements must be included in the NSR permit. A FOP will include it’s own CAM and PM requirement that are independent on the CAM and PM included in the NSR permit.
PM Ask yourself the following questions: Does the rule contain sufficient monitoring? Does it have a sufficient monitoring frequency? If you answered ‘No’ at least once, you will need PM requirements.
CAM Emissions Limit + Control Device + Pre-control ≥ Major CAM applies!
Although NSR is incorporated by reference in Title V, CAM and PM for NSR requirements must be included in the NSR permit. The boilerplate language is designed to satisfy both CAM and PM, although permit specific language may be needed.
As you may be aware, starting June 1, all case-by-case NSR permit applications will require use of the NSR permit application workbook. This workbook is designed to help you prepare a complete NSR permit application, resulting in a more efficient case-by-case permitting process. In regards to NSR and Title V, the workbook contains built-in features that will identify MRRT type requirements that may be required in your permit to demonstrate compliance with the Special Conditions and MAERT limits listed in the NSR.
NSR requirements similar to those found in Title V include [NEXT] CAM and PM, [NEXT] monitoring and testing, [NEXT] and reporting and recordkeeping requirements. As mentioned before, these requirements are detailed within the NSR permit application workbook and helps to ensure that all of the requirements are adequately addressed.
Now, you may be asking “Why CAM and PM?” CAM and PM may be added to some NSR permits if the permit has insufficient (or no) monitoring, recordkeeping, reporting, or testing to assure compliance with standards and proper operation of the control devices; This includes work practice standards, emission limitations, control requirements, and representations in application. Important aspects of monitoring include the parameters, frequency, averaging time, deviation threshold, QA/QC, and recordkeeping. Any CAM and PM that may be added to demonstrate compliance with NSR permit requirements must be included in the NSR permit. It is important to note that Title V can include it’s own CAM and PM requirements that are independent of the CAM and PM requirements included in the NSR.
So, although NSR is incorporated by reference in Title V, CAM and PM for NSR requirements must be included within the NSR permit as well. The boilerplate language is designed to satisfy both CAM and PM, although permit specific language may be needed. [NEXT]

## Slide 20: Major NSR Summary Table in FOP
Permit Number: 99999/N9999 Issuance Date: 05/01/2010 |  |  |  |  |  |  | 
Emission Point Number | Source Name | Air Contaminant Name | Emission Rates |  | Monitoring/ Testing Req. | Recordkeeping Req. | Reporting Req.
 |  |  | lb/hr | TPY | Spec. Cond. | Spec. Cond. | Spec. Cond.
BOIL-Y1801 | 30-Barg Boiler | NOx | 1.99 | 8.72 | 3, 24, 26, 32 | 3, 24, 26, 32 | 3, 24, 26
 |  | SO2 | 0.29 | 1.28 | 24 | 3, 24 | 3, 24
 |  | CO | 13.93 | 30.5 | 24, 26, 32 | 24, 26, 32 | 24, 26
 |  | PM | 1.54 | 6.76 | 21, 24 | 3, 24 | 3, 24
 |  | VOC | 1.09 | 4.79 | 24 | 24 | 24
MRRT Requirements Referencing NSR Special Conditions
MAERT
EPN
Source Name
Air Contaminant Name
Emission Rates
Notes: Title V – Major NSR Summary Table
Shown here is a Major NSR Summary Table in a FOP that is required for sites which have a NA/PSD permit. The table summarizes emission rates, monitoring, recordkeeping, reporting, and testing (MRRT) requirements referenced in the NSR special conditions for each emission point and each pollutant listed in the NA/PSD permit.
The table is constructed by including the Maximum Allowable Emission Rate Table (MAERT) of the NSR Permit with Emission Point Number (EPN), Source Name, Air Contaminant Name, Maximum Allowable Emission Rates (in both lb/hour and tpy) as starting point and then adding MRRT requirements which are referenced in the Special Conditions of the NSR Permit for each EPN.
Includes the following information which is located on the Maximum Allowable Emission Rate Table (MAERT) of the NSR Permit:
Emission Point Number (EPN)
Source Name
Air Contaminant Name
Maximum Allowable Emission Rates (in both lb/hour and tpy)
Also includes monitoring, testing, recordkeeping, and reporting requirements which are referenced in the Special Conditions of the NSR Permit.
Shown here is a Major NSR Summary Table in a Federal Operating Permit which is required for sites that have a Nonattainment or PSD permit. The table summarizes emission rates and MRRT requirements referenced in the NSR special conditions for each emission point, and each pollutant that is listed in the Nonattainment or PSD permit. [NEXT]
The table is constructed by including the Maximum Allowable Emission Rate Table of the NSR Permit. [NEXT]
This shows the Emission Point Number (EPN), [NEXT]
Source Name, [NEXT]
Air Contaminant Name, [NEXT]
and Maximum Allowable Emission Rates (in both lb/hour and tpy) as starting point; [NEXT]
then adds MRRT requirements that are referenced in the Special Conditions of the NSR Permit for each EPN. [NEXT]

## Slide 21: FOP and NSR Project Terminology
Permit Action | FOP Project Type | NSR Project Type
FOP and NSR Project Terminology
Initial permit issuance
Changes/
Modifications
Permit renewal
Expedited actions
Initial
Initial
Notification
Admin. Revision
Minor Revision
Significant Revision
Alteration
Amendment
Changes to Qualified Facilities
Renewal
Renewal
Renewal Certification
Expedited
Expedited
Notes: NSR and FOP Project Terminology:
Before we get into the examples, there are some minor differences in NSR and FOP Project Terminology that you may need to get familiar. For FOP projects, changes and modifications at the site are typically processed as various revision types – administrative, minor and significant depending on the type of change. A notification project does not change the FOP but documents the off-permit change at the site. For NSR projects changes and modifications at the site are typically processed as alteration or amendment projects.
FOP
Initial
Notification
Administrative: Correct typographical errors, identifies/updates administrative information like name, address, or phone number. Can also be an increase in the monitoring frequency. The common practice is to submit multiple Administrative revisions at once. 30 TAC §122.211 can be found at http://texreg.sos.state.tx.us/public/readtac$ext.TacPage?sl=R&app=9&p_dir=&p_rloc=&p_tloc=&p_ploc=&pg=1&p_tac=&ti=30&pt=1&ch=122&rl=211.
Minor: Updates to applicable requirements that are either unit specific or site-wide, add or remove units, remove a PBR or NSR authorization, update NSR authorizations due to permitting actions (excluding PSD/NNSR), remove permit shields. 30 TAC §122.215 can be found at http://texreg.sos.state.tx.us/public/readtac$ext.TacPage?sl=R&app=9&p_dir=&p_rloc=&p_tloc=&p_ploc=&pg=1&p_tac=&ti=30&pt=1&ch=122&rl=215.
Significant: Updates to PSD/NNSR permits due to permit modification, additions or changes to permit shields, significant changes to monitoring requirements or relaxation of reporting/recordkeeping requirements, compliance plan changes or additions. 30 TAC §122.219 can be found at http://texreg.sos.state.tx.us/public/readtac$ext.TacPage?sl=R&app=9&p_dir=&p_rloc=&p_tloc=&p_ploc=&pg=1&p_tac=&ti=30&pt=1&ch=122&rl=219.
Expedited
NSR
Initial
Alteration - addressed in 30 TAC §116.116(c); requested if there is a change from a representation in an application, general condition, or special condition in a permit that does not cause: change in the method of control of emissions; change in the character of emissions; or increase in actual or allowable emissions; requires just a letter of the request and any supporting technical information to APD for approval.
Amendment - addressed in 30 TAC §116.116(b); can be requested when proposed modifications to a permitted facility do not meet a PBR or SP. Required when the modification will cause change in the method of control of emissions; change in the character of emissions; or increase in actual or allowable emissions; submit Form PI-1 and supplemental information; approval is required before any changes can occur; address any PBRs or SPs being incorporated.
Changes to Qualified Facilities – SB1126
Renewal - renewal requirements addressed in 30 TAC §116, Subchapter D; compliance history review conducted on both the site and company prior to issuance of renewal; permits are issued in 10-year cycles. At non-federal sources, permits may contain a provision requiring renewal between five and ten years [30 TAC §116.315(d)(3)]
Renewal Certification - an abbreviated review option is available. The permit must not require adjustments to the conditions or Maximum Allowable Emission Rates Table (MAERT) (i.e., no corrections to emission estimates or factors). If required, CAM must already be in place. The renewal must meet other criteria as identified in Section VII (Renewal Certification Option) of the Form PI-1R.
Expedited - Additional TCEQ resources are used to process the above permit actions.
Before we move on into the examples, lets go over the FOP and NSR project terminology that will be used, since there are some minor differences between the two: [NEXT]
Both projects have the same terminology for initial permits. [NEXT] There are, however, minor differences when looking at changes and modifications to a permit.
For FOP projects; changes and modifications at the site are typically processed as various revision types – known as administrative, minor, and significant - depending on the type of change. A notification project does not change the FOP, but rather it documents the off-permit change at the site. For NSR projects, changes and modifications at the site are typically processed as alteration, amendment, or as a changes to qualified facilities project. [NEXT]
Regarding renewals:
The FOP renewal timeframe is once every 5 years; while renewals for NSR are issued in 10-year cycles, after a compliance history review of both the site and company.
A Renewal Certification is an abbreviated review option that is available for NSR. For this option, the permit must not require adjustments to the conditions or MAERT (i.e., no corrections to emission estimates or factors). If required, CAM must already be in place. The renewal must also meet other criteria as identified in Section VII (Renewal Certification Option) of the Form PI-1R. [NEXT]
Both FOP and NSR allow for expedited actions, during which additional TCEQ resources are used to process these listed permit actions. [NEXT]

## Slide 22: Changes to Permits (Site is a Minor NSR source)
FOP Change
Administrative, minor, or significant change
NSR alteration or amendment issued?
NSR Permit Change
Alteration, amendment, or major source?
Change in process, operation, control, equipment or regulation
Notes: Changes to Permits
After initial permit issuance, proposed changes at a minor NSR site or changes in applicable requirements may result in the need to authorize the change by an NSR permit alteration or amendment and subsequently revise the Title V permit. Changes at a site may include:
addition or removal of emission sources (resulting from a NSR Permit alteration or amendment);
operational changes; or
changes to existing monitoring, reporting, recordkeeping, and testing requirements identified in the permit.
Note that these changes must be already authorized under an issued NSR Permit alteration or amendment before construction can begin.
Once the NSR permit changes have been made and permit is issued, FOP changes may be made through an administrative, minor or significant revision application based on the type of change. If the NSR permit is still pending the site may not go to public notice or announcement until the NSR permit is issued.
The applicable requirements may need to be changed due to one or more of the following reasons:
promulgation of new state or federal regulations;
changes to existing regulations codified in the permit;
new NSR authorizations; or
changes (alterations, amendments, modifications, etc.) to existing NSR authorizations.
Let’s take a look at what changes to permits may occur for a couple of scenarios. In this first example, the site is a minor NSR source.
After initial permit issuance, proposed changes at a minor NSR site, or changes in applicable requirements, may result in the need to authorize the change by an NSR permit alteration or amendment. [NEXT] The change may cause the site to become a major source under Title V and NSR. [NEXT] This change would then require a new or revised Title V permit.
Changes at a site may include:
The addition or removal of emission sources (resulting from a NSR Permit alteration or amendment);
operational changes; or
changes to existing monitoring, reporting, recordkeeping, and testing requirements identified in the permit.
It is important to note that these changes must be already authorized under an issued NSR Permit alteration or amendment before construction can begin. Once the NSR permit changes have been made and permit is issued, FOP changes may be made through an administrative, minor, or significant revision, based on the type of change. If the NSR permit is still pending, the site may not go to TV public notice or announcement until the NSR permit is issued.
The applicable requirements may need to be changed due to one or more of the following reasons:
promulgation of new state or federal regulations;
changes to existing regulations codified in the permit;
new NSR authorizations; or
changes (alterations, amendments, modifications, etc.) to existing NSR authorizations.[NEXT]

## Slide 23: Changes to Permits (Site has a PSD/NA permit)
FOP Change
Administrative, minor, or significant change
NSR alteration or amendment or PSD/NA revised version issued?
Changes to Major NSR Summary Table?
NSR Permit Change
Alteration, amendment, or major modification
Change in process, operation, control, equipment or regulation
Notes: Changes to Permits
After initial permit issuance, proposed changes at a major NSR site or changes in applicable requirements may result in the need to authorize the change by an NSR permit alteration or amendment or major modification and subsequently revise the Title V permit. Note that these changes must be already authorized under an issued NSR Permit alteration or amendment or major modification before construction can begin. Changes at a site may include:
addition or removal of emission sources (resulting from a NSR Permit alteration or amendment);
operational changes; or
changes to existing monitoring, reporting, recordkeeping, and testing requirements identified in the permit.
Once the NSR permit changes have been made and permit is issued, FOP changes may be made through an administrative, minor or significant revision application. The FOP changes may include changes to the Major NSR Summary Table. If the NSR permit is still pending the site may not go to public notice or announcement until the NSR permit is issued.
The applicable requirements may need to be changed due to one or more of the following reasons:
promulgation of new state or federal regulations;
changes to existing regulations codified in the permit;
new NSR authorizations; or
changes (alterations, amendments, modifications, etc.) to existing NSR authorizations.
Now we will consider a site that has a PSD or nonattainment permit:
Similar to the first example, [NEXT] after initial permit issuance, proposed changes at a major NSR site, or changes in applicable requirements, may result in the need to authorize the change by an NSR permit alteration, amendment, or major modification. [NEXT] This would trigger the need to revise the Title V permit.
Again, note that these changes must be already authorized under an issued NSR Permit change before construction can begin. Changes at a site may include: The addition or removal of emission sources; operational changes; or changes to existing monitoring, reporting, recordkeeping, and testing requirements identified in the permit.
Once the NSR permit changes have been made and the NSR permit is issued, FOP changes may be made through an administrative, minor, or significant revision application. The FOP changes may include changes to the Major NSR Summary Table. Once again, if the NSR permit is still pending the site may not go to TV public notice or announcement until the NSR permit is issued. [NEXT]

## Slide 24: Changes to Permits (Site has a PSD/NA permit)
Potential FOP Change
Improved monitoring
Improved demonstration of compliance
Changes to NSR Permit?
NSR Permit Change
Alteration or amendment to address potential NSR deficiency
EPA or
Public Comments Asserting FOP Deficiency
Notes: Changes to Permits: For site has a PSD/NA permit
As shown on earlier slides, changes in NSR permit usually trigger a change in the FOP. However, in some cases, changes to FOP may cause changes in the NSR permit. For example, a FOP permit may receive comments from EPA or public during the comment period asserting FOP or NSR permit deficiency exists in certain aspects of the permit such as monitoring and demonstration of compliance with applicable requirements. TCEQ may conduct a technical and legal analysis of the comments and assertions and may determine that the FOP may need to be changed to improve monitoring and demonstration of compliance with applicable requirements. If the improvements affect the NSR permit then NSR permit changes must be made by applicant to the NSR permit.
As shown in previous two examples, changes in the NSR permit usually trigger a change in the FOP. However, in some cases, changes to FOP may trigger changes in the NSR permit. For example: a FOP may receive comments from EPA or the public during their respective comment periods, asserting that a FOP or NSR permit deficiency exists in certain aspects of the permit. This can be in regards to monitoring or a demonstration of compliance with applicable requirements. [NEXT] TCEQ may conduct a technical and legal analysis of the comments and assertions, and may determine in some cases that the FOP needs to be changed to clarify or improve monitoring or to demonstrate compliance with applicable requirements. [NEXT] If the improvements affect the NSR permit, then the applicant must submit a permit alteration or amendment to make those changes to the NSR permit, and address the asserted deficiencies. [NEXT]

## Slide 25: Example: New Source Review Authorization References in Title V
Prevention of Significant Deterioration (PSD) Permits | 
PSD Permit No.: PSDTX9999 | Issuance Date: 05/01/2019
Title 30 TAC 116 Permits, Special Permits, and other Authorizations | 
Authorization No.: 99999 | Issuance Date: 05/01/2019
Permits By Rule (30 TAC Chapter 106) for the Application Area | 
Number: 106.261 | Version No./Date: 11/01/2003
Number: 106.262 | Version No./Date: 11/01/2003
New Revision Date
New Revision Date
Example: New Source Review Authorization References in FOP
Notes: Example
As a minimum, change to FOP that is triggered by a change to the NSR permit may simply involve changing the issuance date of the NSR permit alternation or amendment or modification permit.
So, what happens when an NSR permit changes? Typically it triggers a change in the FOP. [NEXT]
At a minimum, it may involve just changing the issuance date of the NSR permit alteration, amendment, or modification in the NSR Authorization References table, which is found in the FOP. [NEXT]
In the next part of our presentation, my colleague Vasant Chaphekar will show us some examples which describe various changes a site may undergo, and discuss the impact of these changes on FOP and NSR permits. [NEXT]

## Slide 26: Examples
Examples
Summary
New Site
Minor NSR Site
Major NSR Site
PBR authorization
Alteration or amendment
Modification to PSD/NA permit
How do FOP actions affect NSR?
How do NSR permit actions affect FOP?
Interaction
Notes: In the next several slides, we will describe various types of changes that a site may undergo and discuss the impact of these changes on NSR and FOP permits. The 3 types of sites considered are: new site that is authorized by a PBR, a minor NSR site and a major NSR site. In the examples, we will also look at how an NSR permit action affects the FOP and vice versa.
Thank you Ariel. In the next several slides, we will look at three types of sites: a new site that is authorized by a PBR [NEXT], a minor NSR site [NEXT], and a major NSR site [NEXT]. We will also look at how a proposed change or modification at a site affects an NSR permit action which in turn affects the FOP, and vice versa. [NEXT]

## Slide 27: Example: New Site – Attainment Area
Based on available info,
is site subject to TV? (T/F)
Actual NOX = 50 tpy
PBR 106.512 (Registered Y/Certified N)
ENGINE
> 240 HP
T
Notes: Example: New Site – Attainment Area
In this example, we have a new engine unit located at a new site located in an attainment area. Engine has a HP rating > 240. It is authorized under PBR 106.512, which was registered by the applicant but applicant did not certify the PBR. Actual NOx emissions at the site were 50 tpy based on test data. Note that operating speed and hours of operation for this source is not known. Based on the available info is the site subject to TV permit requirements? True or False. Answer is True since the applicant did not certify emission levels for NOx or any other pollutant, the default emission limits for all PBRs is defined in 30 TAC 106.4. Thus, PTE for the unit is 250 tpy NOx. The site is therefore a major source under 30 TAC 122 and requires a FOP.
Image Attribution:
Engine by anbileru adaleru from the Noun Project https://thenounproject.com/search/?q=engine&i=780259
In this example, we have a new engine unit that is being installed at a new site located in an attainment area. Engine has a HP rating > 240. It is authorized under PBR 106.512, which was registered by the applicant but applicant did not certify the PBR. Actual NOx emissions at the site were 50 tpy based on test data. Based on the available info is the site subject to TV permit requirements? True or False. Answer is True since the applicant did not certify emission levels for NOx or any other pollutant, the default emission limits for all PBRs is defined in 30 TAC 106.4. Thus, PTE for the unit is 250 tpy NOx. The site is therefore a major source under 30 TAC 122 and requires a FOP.

## Slide 28: Impact on NSR and FOP Permitting
  NSR – No impact under Chapter §116
  Applicant may consider submitting PI-7-CERT or APD-CERT form to certify PTE of NOx emission sources is < 100 tpy to avoid FOP trigger; or
  Submit initial application for a FOP
Example: New Site – Attainment Area
Notes: Since the unit was authorized under PBR 106.512, there is no impact on NSR permitting under 30 TAC 116. Applicant may consider submitting PI-7-CERT or APD-CERT to certify PTE of NOx emission sources is <100 tpy to avoid FOP trigger. If no PI-7-CERT can be submitted to certify NOx emission levels are below 100 tpy then the applicant must submit initial application for a FOP.
Since the unit was authorized under PBR 106.512, there is no impact on NSR permitting under 30 TAC 116. Applicant may consider submitting PI-7-CERT to certify that PTE of NOx emission sources is < 100 tpy to avoid FOP trigger. If no PI-7-CERT can be submitted to certify that NOx emission levels are below 100 tpy then the applicant must submit an initial application for a FOP.

## Slide 29: Example: New Site – Attainment Area, when to submit an application
  NSR – before construction begins; construction cannot occur until the permit is issued
  FOP – before operation begins
Example: New Site – Attainment Area
When to Submit an Application
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued and for FOP permit – before operation begins.
When to submit an application? For NSR permit – before construction begins and for FOP permit – before operation begins.

## Slide 30: Example: Minor NSR Site Un-named Source - Attainment Area - NOT Previously Subject to TV
Subject to TV? (T/F)
Subject to PSD review? (T/F)
NOX increased from 50 tpy to 100 tpy
Throughput increase
F
T
Notes: Example: Minor NSR Site (Un-named source located in an attainment area and not previously subject to Title V
In this example, we have a minor NSR site with an un-named source located in an attainment area. The site was not previously subject to a TV permit. Due to increased production and process changes NOx emission for a unit increased from 50 tpy to 100 tpy. Is the NSR amendment project subject to PSD review? True or False. False because source with PTE = 100 tpy is not a major NSR source in an attainment area. Is the site subject to a TV permit? True or False. True because source with PTE = 100 tpy is a major source under 30 TAC 122.
Image Attribution:
https://www.freeimages.com/photo/refinery-row-2-1545671
In this example we have a Minor NSR Site that includes an un-named source located in an attainment area and the site was not previously subject to Title V. As described earlier by Ariel, an ‘unnamed source’ is a source that is not listed in 30 TAC §122.10(13)(C) or §116.164(a)(1). Due to increased production and process changes NOx emission for a unit increased from 50 tpy to 100 tpy. Is the NSR amendment project subject to PSD review? True or False. [NEXT] False because source with PTE = 100 tpy is not a major NSR source in an attainment area. Is the site subject to a TV permit? True or False. [NEXT] True because source with PTE = 100 tpy is a major source under 30 TAC 122. [NEXT]

## Slide 31: Example: Minor NSR Site Un-named Source - Attainment Area - NOT Previously Subject to TV, Impact on NSR and FOP Permitting
  NSR – File an amendment to revise NSR
  Not a major modification
  Submit initial application for a FOP
Impact on NSR and FOP Permitting
Example: Minor NSR Site Un-named Source - Attainment Area - NOT Previously Subject to TV
Notes: How does this change affect NSR and TV permitting actions?
NSR – File an amendment to revise NSR.
Not a major modification since site is a minor source.
Site must submit initial application for a FOP.
How does this change affect NSR and TV permitting actions?
Applicant will have to file an amendment to revise NSR.
This amendment is not considered as a major modification since PTE for NOx source at the site is still below a major NSR source.
Since the site was previously not subject to a Title V permit but is now a major source under Chapter 122 after the NSR amendment is issued, the site must submit an initial application for a FOP. [NEXT]

## Slide 32: When to Submit an Application
  NSR – before construction begins; construction cannot occur until the permit is issued
  FOP – before operation begins
Example: Minor NSR Site Un-named Source - Attainment Area - NOT Previously Subject to TV
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued and for FOP permit – before operation begins.
When to submit an application? For NSR permit – before construction begins and for FOP permit – before operation begins. [NEXT]

## Slide 33: Example: Minor NSR Site Un-named Source - Attainment Area - Subject to TV
Type of FOP revision? Admin./Minor/Significant?
Update NSR and FOP? (Y/N)
NOX increased from 50 tpy to 100 tpy
Throughput increase
Y
Minor
Notes: Minor NSR Site (un-named source in an attainment area and previously subject to Title V)
In this example, we have a minor NSR site with an un-named source located in an attainment area. The site is subject to a TV permit. Due to increased production and process changes NOx emission for a unit increased from 50 tpy to 100 tpy. Does the applicant need to submit an NSR and FOP application to revise their permits? Yes or No. Answer is Yes since NSR amendment must be approved before construction can begin. What type of FOP revision project is required to be submitted? Admin./Minor/Significant? Answer is Minor revision project since it meets the qualification criteria under 30 TAC §122.215.
Image Attribution:
https://www.freeimages.com/photo/refinery-row-2-1545671
In this example, we have a Minor NSR Site that includes an un-named source. The site is located in an attainment area and the site is currently operating under a Title V permit. Due to increased production and process changes NOx emissions for a unit increased from 50 tpy to 100 tpy. Question: Does the applicant need to submit an NSR and FOP application to revise their permits? Yes or No. [NEXT]
Answer is Yes since NSR amendment must be approved before construction can begin and a change is NSR typically results in making changes to the FOP. What type of FOP revision project is required to be submitted? Admin./Minor/Significant? [NEXT] Answer is Minor revision project since it meets the qualification criteria under 30 TAC §122.215. [NEXT]

## Slide 34: Example: Minor NSR Site Un-named Source - Attainment Area - Subject to TV, Impact on NSR and FOP Permitting
  NSR – File an amendment to revise NSR
  Not a major modification
  FOP – Submit a FOP minor revision application upon issuance of NSR amendment
Impact on NSR and FOP Permitting
Example: Minor NSR Site Un-named Source - Attainment Area - Subject to TV
Notes: How does this change affect NSR and TV permitting actions?
NSR – File an amendment to revise NSR.
Not a major modification since site is a minor source.
Site must submit a FOP minor revision application upon issuance of NSR amendment.
How does this change affect NSR and TV permitting actions?
Applicant will have to file an amendment to revise NSR. This amendment is not considered as a major modification since PTE for NOx source at the site is still below a major NSR source.
Since the site already has a FOP, it must submit a FOP minor revision application upon issuance of NSR amendment to incorporate the changes. [NEXT]

## Slide 35: Example: NSR Authorization References in Title V
Title 30 TAC 116 Permits, Special Permits, and other Authorizations | 
Authorization No.: 99999 | Issuance Date: 05/01/2019
Permits By Rule (30 TAC Chapter 106) for the Application Area | 
Number: 106.261 | Version No./Date: 11/01/2003
Number: 106.262 | Version No./Date: 11/01/2003
New Revision Date
Example: New Source Review Authorization References in FOP
Notes: Example: NSR Authorization References
The FOP minor revision project may be as simple as revising the issuance date of the NSR permit.
In some cases, the FOP minor revision project may be as simple as revising the issuance date of the NSR permit.

## Slide 36: Example: New Source Review Authorization References When to Submit an Application
  NSR – before construction begins; construction cannot occur until the permit is issued.
  FOP – before operation begins; can operate the unit before FOP is issued
When to Submit an Application
Example: New Source Review Authorization References
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued. For FOP – before operation begins. However, site can operate the unit before FOP is issued.
When to submit an application? For NSR permit – before construction begins. As is true for any NSR permit, construction at site cannot occur until the NSR permit is issued. For FOP – the minor revision application must be submitted before operation begins. Since the changes are minor under 30 TAC §122.215, site can operate the unit that is being modified after the application is submitted and before the FOP minor revision is issued. [NEXT]

## Slide 37: Example: Minor NSR Site HGB/DFW Area – Site was NOT Subject to TV
Subject to TV? (T/F)
Subject to PSD/NA review? (T/F)
NOX increased from 45 tpy to 150 tpy
Throughput increase
T
T
Notes: Minor NSR Site (HGB/DFW area, previously not subject to Title V)
In this example, we have a minor NSR site located in a non-attainment area (HGB/DFW). The site was not previously subject to a TV permit. Due to increased production and process changes NOx emission for a unit increased from 45 tpy to 150 tpy. Is the NSR amendment project subject to NA review? True or False. True because source with PTE = 150 tpy is a major NSR source in the NA area per current moderate classification. Is the site subject to a TV permit? True or False. True because source with PTE = 100 tpy is a major source under 30 TAC 122.
Image Attribution:
https://www.freeimages.com/photo/refinery-row-2-1545671
In this example, we have a minor NSR site located in a non-attainment area (e.g., HGB/DFW). The site was not previously subject to a TV permit. Due to increased production and process changes NOx emission for a unit increased from 45 tpy to 100 tpy. Is the NSR amendment project subject to NA review? True or False. [NEXT] True because source with PTE = 100 tpy is a major NSR source in the NA area per current “moderate” area classification. Is the site subject to a TV permit? True or False. [NEXT] True because source with PTE = 100 tpy is a major source under 30 TAC 122. [NEXT]

## Slide 38: Example: Minor NSR Site HGB/DFW Area - Site was NOT Subject to TV, Impact on NSR and FOP Permitting
  NSR – File an amendment to revise NSR
  Major modification project
    Submit NA permit application
  Submit initial FOP application upon issuance of NA permit
  Include Major NSR Summary Table in FOP
Impact on NSR and FOP Permitting
Example: Minor NSR Site HGB/DFW Area - Site was NOT Subject to TV
Notes: How does this change affect NSR and TV permitting actions?
NSR – File an amendment to revise NSR.
Project is considered as a major modification since source is a major source in NA area per current threshold levels.
Site must submit an initial FOP application upon issuance of NSR NA permit.
FOP initial application must include a Major NSR Summary Table for the NA permit.
How does this change affect NSR and TV permitting actions?
NSR – File an amendment to revise NSR.
Project is considered as a major modification since source is a major source in NA area per current threshold levels. In its NSR amendment application, applicant must submit NSR workbook data that includes netting and offset calculations that may be required for federal review.
Since site was not previously subject to a Title V permit, it must also submit an initial FOP application upon issuance of NSR NA permit. The FOP initial application must include a Major NSR Summary Table for the NSR NA permit. [NEXT]

## Slide 39: Example: Minor NSR Site HGB/DFW Area - NOT Previously Subject to TV , When to Submit an Application
  NSR – before construction begins; construction cannot occur until the permit is issued.
  FOP – upon issuance of the NSR NA permit and before operation begins; can operate the unit before FOP is issued
When to Submit an Application
Example: Minor NSR Site HGB/DFW Area - NOT Previously Subject to TV
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued. For FOP – upon issuance of the NSR NA permit and before operation begins. However, site can operate the unit before FOP is issued.
When to submit an application? For NSR permit – before construction begins. As is true for any NSR permit, construction cannot occur until the permit is issued.
The site must submit an initial application for a FOP upon issuance of the NSR NA permit and before operation begins. The initial FOP application may be submitted as an abbreviated or a complete application. Once the initial FOP application has been submitted, the site can operate the unit before FOP is issued. [NEXT]

## Slide 40: Example: Major NSR Site Site is Subject to TV
Type of FOP revision - Minor/Significant?
New or Updated NSR/PSD/NA permit version
Major modification project
Add new units and throughput increase
Significant
Notes: Major NSR Site and subject to Title V
In this example, we have a major NSR site that is subject to a TV permit. Due to increased production and process changes applicant submitted an NSR project which is considered a major modification. Applicant has submitted a new federal permit application or is updating a previously issued NSR/PSD/NA permit version. What type of FOP revision project is required to be submitted? Admin./Minor/Significant? Answer is Significant revision project since the NSR modification is considered as a Title I modification and it meets the qualification criteria under 30 TAC §122.219.
Image Attribution:
Photo 257700.jpeg from Pexels.com
In this example, we have a major NSR site that is subject to a TV permit. Due to increased production and process changes applicant submitted an NSR project application which is considered a major modification. Applicant has submitted an NSR amendment that is subject to federal review. The major source may obtain a new federal permit or may update a previously issued NSR/PSD/NA permit version. What type of FOP revision project is required to be submitted? Admin./Minor/Significant? [NEXT] Answer is Significant revision project since the NSR modification is considered as a Title I modification and it meets the qualification criteria under 30 TAC §122.219. [NEXT]

## Slide 41: Impact on NSR Permitting
  NSR – File an amendment to revise NSR
    Major modification project
    Submit NA application
    Revise version number of NA permit
Example: Major NSR Site Site is Subject to TV
Notes: How does this change affect NSR permitting actions?
NSR – File an amendment to revise NSR
Major modification Project
Submit NA application
Revise version number of NA permit if site has a NA permit
How does this change affect NSR permitting actions?
For NSR permit, applicant must file an amendment to revise the NSR permit. Since the amendment is a major modification project, applicant may need to submit additional information such as netting and offset calculations for issuance of the NSR NA permit. If site already has a NA permit, this project would revise the version number of NA permit, e.g., N9999 to N9999M1. If site does not have a NA permit, a new NSR NA permit would be issued to the site. [NEXT]

## Slide 42: Impact on FOP Permitting
  FOP - Submit a FOP significant revision application
    Revise or add Major NSR Summary Table in FOP
    Revise or add version number of NSR/PSD/NA permit in FOP table
Example: Major NSR Site Site is Subject to TV
Notes: How does this change affect FOP permitting actions?
Submit a FOP significant revision application
Revise or add Major NSR Summary Table in FOP
Revise or add version number of NSR/PSD/NA permit in FOP table
How does this change affect FOP permitting actions?
Since the NSR action involves a Title I modification, it is considered as a significant revision under 30 TAC §122.219. Applicant would need to submit a FOP significant revision application. Along with this application, applicant will revise or add Major NSR Summary Table in FOP including updating or adding a NSR/PSD/NA permit revision number. [NEXT]

## Slide 43: Example: Major NSR Site Site is Subject to TV , When to Submit an Application
  NSR – before construction begins; construction cannot occur until the permit is issued.
  FOP – before operation begins
    No TV authorization to operate unit until FOP is issued
    No public notice until NSR NA permit is issued
When to Submit an Application
Example: Major NSR Site Site is Subject to TV
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued. For FOP – upon issuance of the NSR NA permit and before operation begins. No TV authorization to operate the unit until FOP is issued. FOP cannot go to public notice till NSR NA permit is issued.
When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued. For FOP – upon issuance of the NSR NA permit and before operation begins. In a FOP significant revision project, applicant does not have TV authorization to operate the unit until FOP is issued and FOP cannot go to public notice till NSR NA permit is issued. [NEXT]

## Slide 44: Example: Major NSR Site, Site is Subject to Title V, Minor Modification Project
Type of FOP revision - Minor/Significant?
Update NSR/PSD/NA permit
Minor modification project
Add new units and throughput increase
Minor
Example: Major NSR Site Site is Subject to TV
Notes: Major NSR Site and subject to Title V
In this example, we have a major NSR site that is subject to a TV permit. Due to increased production and process changes applicant submitted an amendment NSR project which is not considered as a major modification. There is no change to the previously issued NSR/PSD/NA permit version. What type of FOP revision project is required to be submitted? Admin./Minor/Significant? Answer is Minor revision project since the NSR modification is not considered as a Title I modification and it meets the qualification criteria under 30 TAC §122.215.
Image Attribution:
Photo 257700.jpeg from Pexels.com
In this example, we have a major NSR site that is subject to a TV permit. Due to increased production and process changes applicant submitted an NSR amendment project which is not considered as a major modification. There is no change to the previously issued NSR/PSD/NA permit version. What type of FOP revision project is required to be submitted? Admin./Minor/Significant? [NEXT] Answer is Minor revision project since the NSR modification is not considered as a Title I modification and it meets the qualification criteria under 30 TAC §122.215. [NEXT]

## Slide 45: Impact on NSR/PSD/NA Permit
  NSR – File an amendment to revise NSR
    Revise Special Conditions
    Revise MAERT
    No change in NSR/PSD/NA permit version
Example: Major NSR Site Site is Subject to TV
Notes: How does this change affect NSR permitting actions?
NSR – File an amendment to revise NSR special conditions and MAERT as applicable
No a major modification project and no change in NSR/PSD/NA permit version number
How does this change affect NSR permitting actions?
For NSR permit, applicant must file an amendment to revise the NSR permit special conditions and MAERT as applicable. Since this project is not a major modification there is no change in NSR/PSD/NA permit version number. [NEXT]

## Slide 46: Example: Major NSR Site, Site is subject to Title V, Impact on FOP Permitting due to NSR Action
  FOP - Submit a FOP minor revision application upon issuance of NSR /PSD/NA amendment
    Revise Major NSR Summary Table in FOP
    Revise or add issuance date of NSR/PSD/NA permit in FOP table
Impact on FOP Permitting due to NSR Action
Example: Major NSR Site Site is Subject to TV
Notes: How does this change affect FOP permitting actions due to NSR permit changes?
Submit a FOP minor revision application upon issuance of NSR /PSD/NA amendment
Revise Major NSR Summary Table in FOP
Revise NSR/PSD/NA permit reference in FOP table
How does this change affect FOP permitting actions due to NSR permit changes?
To revise their FOP, applicant needs to submit a FOP minor revision application upon issuance of NSR/PSD/NA amendment. If there are any changes in the NSR special conditions or MAERT then applicant needs to revise the Major NSR Summary Table in FOP. If there are no changes to the NSR special conditions or MAERT then as a minimum the issuance date of the NSR/PSD/NA permit referenced in Major NSR Summary table should be revised. [NEXT]

## Slide 47: Example: Major NSR Site Site is Subject to TV , Minor Modification Project, When to Submit an Application
  NSR – before construction begins ; construction cannot occur until the permit is issued
  FOP – before operation begins
When to Submit an Application
Example: Major NSR Site Site is Subject to TV
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued and for FOP permit – before operation begins.
When to submit an application? For NSR permit – before construction begins and for FOP permit – before operation begins. Since the changes are minor under 30 TAC §122.215, site can operate the unit before the FOP minor revision is issued. [NEXT]

## Slide 48: Example: Major NSR Site, Site is Subject to Title V
May Require NSR Revision – Alteration/Amendment?
Asserted Insufficiency in Demonstration of Compliance with Emission Limits
Asserted Deficiencies in NSR/PSD/NA
FOP Receives EPA or Public Comments
Example: Major NSR Site Site is Subject to TV
Notes: Major NSR Site and subject to Title V
In this example, we have a major NSR site that has a PSD/NA permit and is also subject to a TV permit. During a FOP public notice period, TCEQ receives comments from the EPA or public asserting deficiencies in the NSR permit and hence in the FOP. Specifically, the comment asserts that the NSR permit has insufficient monitoring and does not demonstrate how compliance is achieved with MAERT emission limits. TCEQ may conduct a technical and legal analysis of the comments and assertions and may determine that the applicant may need to submit an NSR permit alteration or an amendment to address the comments.
Image Attribution:
Photo 257700.jpeg from Pexels.com
In this final example, we will illustrate how an action on a FOP project may trigger a change in the NSR permit. We have a major NSR site that has a PSD/NA permit and is also subject to a TV permit. During a public comment period of the FOP, TCEQ receives comments from the EPA or public asserting deficiencies in the NSR permit and hence in the FOP. Specifically, the commenter asserts that the NSR permit lacks sufficient monitoring and the NSR permit does not demonstrate how compliance is achieved with MAERT emission limits. TCEQ may conduct a technical and legal analysis of the comments and may recommend in this specific example that the applicant submit an NSR permit alteration or an amendment to improve monitoring and add emission calculations to address the comments. [NEXT]

## Slide 49: Changes in NSR/PSD/NA Permit
  Revise Special Conditions - including monitoring, testing, recordkeeping and reporting
  Addition of PM/CAM requirements to permit
Example: Major NSR Site Site is Subject to TV
NSR WORKBOOK!
Notes: In response to the EPA or public comments, the changes in the NSR/PSD/NA permit may include revising special conditions including monitoring, testing, recordkeeping and reporting (MRRT), and addition of PM/CAM requirements to the NSR permit. If you can recollect, the NSR workbook contains valuable information about EPN specific MRRT and PM/CAM requirements.
In response to the EPA or public comments, the changes in the NSR/PSD/NA permit may include revising special conditions including monitoring, testing, recordkeeping and reporting (MRRT), and addition of PM/CAM requirements to the NSR permit. As was described earlier by my colleague, the NSR workbook contains valuable information about EPN specific MRRT and PM/CAM requirements. The NSR workbook is part of an NSR application representation and it can be used to address the EPA or public comments.

## Slide 50: Changes to the FOP
  May require minor or significant revision to SOP
  Revise Major NSR Summary Table (if needed)
  Revise NSR/PSD/NA issuance date
Example: Major NSR Site Site is Subject to TV
Notes: Changes to the FOP
May require minor or significant revision to SOP
Revise Major NSR Summary Table (if needed)
Revise NSR/PSD/NA issuance date
Depending on TCEQ’s technical and legal analysis of the comments, recommended changes to the FOP may require minor or significant revision to the FOP. For example, if NSR permit is amended then the Major NSR Summary Table may need to be revised and the issuance date changed. [NEXT]

## Slide 51: Example: Major NSR Site, Site is Subject to Title V, when to submit an application
  NSR – before construction begins ; construction cannot occur until the permit is issued
  FOP – before operation begins
When to Submit an Application
Example: Major NSR Site Site is Subject to TV
Notes: When to submit an application? For NSR permit – before construction begins; construction cannot occur until the permit is issued and for FOP permit – before operation begins.
When to submit an application? For NSR permit – before construction begins and for FOP permit – before operation begins. [NEXT]

## Slide 52: Summary
Examples
Summary
  NSR and Title V – Separately issued permits but need to be synchronized
  Interaction – Change in NSR permit causes a change in the FOP; Public/EPA comment related FOP changes may drive an NSR change
  Site/Permit Interaction – Permit revision process
Interaction
Notes: Summary
To summarize the presentation, an NSR permit is required before construction on a facility begins. The purpose of the NSR program is to issue permits for new construction or modification, establishing emission controls and limits based on applicable state and federal rules and a best available control technology (BACT) and impacts review.
A Title V permit is required for operation of major sources and certain non-major sources. Title V permits codify all applicable air requirements into one authorization. The Title V permit does not authorize any air emissions. In general, Title V permits prescribe monitoring and recordkeeping for determining compliance with applicable requirements, compliance plans for emission units that are not in compliance with applicable requirements, and requirements for permit holders to certify compliance with the permit annually and report any deviations with the permit semi-annually.
NSR and Title V permit are separately issued permits however there is interaction between them. Therefore, they need to be synchronized since NSR permits are incorporated by reference into Title V permit. Changes in the NSR permit triggers a change in the FOP. The FOP change may be processed as an administrative, minor or significant revision. In some cases, FOP changes made due to EPA or public comments may drive a change in the NSR permit.
Finally, as your site goes through changes in process, operation, control equipment or regulation it is imperative that your NSR and TV permits should reflect these changes. You should use the permit revision process and submit your revision, alteration or amendment projects in a timely manner to keep your NSR and TV permits current and active.
To summarize our presentation, an NSR permit is required before construction on a facility begins. The purpose of the NSR program is to issue permits for new construction or modification, establish emission controls and pollutant limits based on applicable state and federal rules using a best available control technology (BACT) and conduct a health impacts review.
A Title V permit is required for authorizing operation of major sources and certain non-major sources. While a Title V permit does not authorize any air emissions, it codifies all applicable air requirements into one authorization. In general, Title V permits document monitoring, testing, reporting and recordkeeping requirements to demonstrate compliance with applicable requirements. Permit holders must certify compliance with all applicable requirements on an annual basis and report any deviations semi-annually.
Although NSR and Title V permit are separately issued permits there is interaction between them. Therefore, they need to be synchronized since NSR permits are incorporated by reference into Title V permit. Changes in the NSR permit typically triggers a change in the FOP. The FOP change may be processed as an administrative, minor or significant revision. In some cases, changes made in the FOP due to EPA or public comments may drive a change in the NSR permit.
Finally, as a site goes through changes in process, operation, control equipment or regulation it is imperative that their NSR and TV permits should reflect these changes on a continuous basis. Applicants should use the permit revision process and submit revision, alteration or amendment projects in a timely manner to keep their NSR and TV permits current and active. This concludes our presentation. [NEXT]

## Slide 53: Thank You!
APD Contacts
Ariel Ramirez
  Ariel.Ramirez@tceq.texas.gov
Vasant Chaphekar, P.E.
  Vasant.Chaphekar@tceq.texas.gov
General
  airperm@tceq.texas.gov
  (512) 239 -1250
Notes: Contacts
Ariel Ramirez
  Ariel.Ramirez@tceq.texas.gov
  (512) 239-4935
Vasant Chaphekar, P.E.
  Vasant.Chaphekar@tceq.texas.gov
  (512) 239-1341
General Air Permitting Contact
  airperm@tceq.texas.gov
  (512) 239-1250
Image Attribution: https://tpwd.texas.gov/newsletters/eye-on-nature/2015fall/page2.phtml
Thank you very much. Any questions?