## Slide 1: Public Water System Supervision Program Quality Assurance Project Plan
Jessica Hoch
Drinking Water Assessment Team Lead
Jessica.Hoch@tceq.texas.gov
512-239-2353
Gary Regner
PWSS Program QA Manager
Gary.Regner@tceq.texas.gov
512-239-4528

## Slide 2: Quality Assurance Project Plan
Quality Assurance and Quality Control processes related to environmental data collection activities
Includes 10 addenda addressing program-specific QA and QC
Revised every 3 years with annual updates
EPA approval
12/20/2017
Last revision 11/4/2016
1st Annual update in 2017
2nd Annual update in 2018

## Slide 3: Quality Assurance Project Plan
Addendum 1 – Sampling, Analysis, and Reporting of Chemical Compliance Data
  Applies to Chemical Compliance laboratories and sample collection contractor only
Addendum 2 – Laboratory Guidance for the Analysis and Reporting of Tap Water Samples under the Lead and Copper Rule
  Applies to labs analyzing Pb/Cu tap samples

## Slide 4: Quality Assurance Project Plan
Addendum 3 – Laboratory Guidance for the Analysis and Reporting of Water Quality Parameters Under the Lead and Copper Rule
  Applies to labs analyzing WQP samples
Addendum 4 – Laboratory Guidance for Analysis and Reporting Under the Revised Total Coliform Rule
  Applies to labs analyzing microbial samples under the RTCR

## Slide 5: Quality Assurance Project Plan
Addendum 5 – Comprehensive Compliance Investigations
  Applies to data collection and management resulting from region conducted CCIs
Addendum 6 – Source Water Susceptibility Assessments
  Applies to source water data collection and management

## Slide 6: Quality Assurance Project Plan
Addendum 7 – Review and Approval of Public Water System Engineering Plans
  Applies to data collection and management related to PWS plans and specifications
Addendum 8 – Texas Optimization Program Evaluations
  Applies to data collection and management from TCEQ performance evaluations (CPE/SPE)

## Slide 7: Quality Assurance Project Plan
Addendum 9 – Acquisition of Treatment Technique and Disinfectant Residual Data
  Applies to data collection and management related to treatment techniques and disinfectant residual monitoring
Addendum 10 – Special Investigation QAPP Template
  Template for TCEQ special investigations that involve sample collection and analysis

## Slide 8: 2017 Annual Updates Addenda Revised
Addendum 2—Guidance for the Analysis and Reporting of Lead and Copper under the Lead and Copper Rule
Addendum 3—Guidance for the Analysis and Reporting of Water Quality Parameters under the Lead and Copper Rule
Addendum 4—Guidance for Analysis and Reporting under the Revised Total Coliform Rules
Notes: All three guidance documents primarily address laboratory requirements for sample receipt, analysis, and reporting. Requirements are program specific and reflect rules and regulations specific to the drinking water program. Laboratories need to be aware there situations in which drinking water rules and regulations applying to laboratories which are more stringent than the TNI Standards. I think most laboratories understand this, but there we received a few questions related to this issue. For example, the TNI specifies the sample label must have a unique identifier only. Appendix A, Figure A-1 of the Certification Manual for Laboratories analyzing Drinking Water has requirements for sample labels which include the sample location, date and time of sample collection, etc… This is more stringent than what the TNI Standard requires, which is why we included it.

## Slide 9: Revisions to Addendum 2 Laboratory Guidance for Analysis and Reporting of Lead and Copper Tap Water Samples
Minor non-substantive revisions made by the TCEQ
Approval page reflects WSD reorganization in Fall 2016
Revised LCR Chain of Custody Form 20683

## Slide 10: Revisions to Addendum 3 Laboratory Guidance for Analysis and Reporting of Water Quality Parameters under the LCR
Most substantive revisions (of the 3) made to this document
Approval page reflects WSD reorganization in Fall 2016
Requires laboratories to analyze all parameters included in the 30 TAC rule update effective March 30, 2017
Alkalinity, conductivity, calcium, chloride, hardness, iron, manganese, pH, sodium, sulfate, temperature, total dissolved solids, and orthophosphate or silica, depending on the inhibitor

## Slide 11: Revisions to Addendum 3 (continued)
Explains how to report results when single samples are analyzed by multiple laboratories
Requires laboratory approval (or accreditation) for original parameters and laboratory accreditation only for additional parameters
Requires initial receiving laboratory to report pH and temperatures as field results in the field measurement portion of the EDD

## Slide 12: Revisions to Addendum 3 (continued)
Provides an example template for an analytical test report.
Includes Chain of Custody Form 20679
References companion document–Public Water System Guidance for Monitoring and Collection of Water Quality Parameters
Updates required information in the analytical test report

## Slide 13: Revisions to Addendum 4 Laboratory Guidance for Analysis and Reporting Under the Revised Total Coliform Rule
Approval page reflects WSD reorganization in Fall 2016
Most significant changes reflect changes to the Sample Receipt section
Addresses problems encountered when sample results are received
Additional revisions reflect issues that laboratories brought to the attention of TCEQ accreditation staff

## Slide 14: 2018 Annual Updates Addenda under current Revision
Addendum 1 – Sampling, Analysis, and Reporting of Chemical Compliance Data
  Includes revisions to the Drinking Water Sampling Guide (DWSG)
  Applies to TCEQ Chemical Compliance Laboratories and Sample Collection Contractor
  Revisions in final draft until Drinking Water Compliance Sampling Services Contract is awarded
Notes: All three guidance documents primarily address laboratory requirements for sample receipt, analysis, and reporting. Requirements are program specific and reflect rules and regulations specific to the drinking water program. Laboratories need to be aware there situations in which drinking water rules and regulations applying to laboratories which are more stringent than the TNI Standards. I think most laboratories understand this, but there we received a few questions related to this issue. For example, the TNI specifies the sample label must have a unique identifier only. Appendix A, Figure A-1 of the Certification Manual for Laboratories analyzing Drinking Water has requirements for sample labels which include the sample location, date and time of sample collection, etc… This is more stringent than what the TNI Standard requires, which is why we included it.

## Slide 15: QAPP Overview
Laboratories are subject to requirements under:
  TNI (Lab Accreditation)
  EPA’s Manual for the Certification of Laboratories Analyzing Drinking Water (MCLADW), 5th Ed.
  State and Federal regulations (TAC, CFR)
In some cases PWSS requirements may be stricter than TNI
The TCEQ (WSD) reserves the right to not use for compliance analytical data that does not meet program requirements

## Slide 16: QAPP Addendum #2
Guidance for the Analysis and Reporting of Tap Water Samples under the Lead and Copper Rule (LCR)
  Applies to PWSs and labs submitting data for compliance under the LCR (tap samples)
  Samples from public water systems
  Includes regulatory and program requirements
  Current Revision 1, effective 12/20/2017

## Slide 17: QAPP Addendum #2
Samples must be analyzed by a laboratory that is accredited in the drinking water matrix using a method acceptable to EPA
Samples must be collected in 1 L lab grade plastic bottles with a fill line
  Acid preservation should be done in the lab
    No later than 14 days after collection

## Slide 18: QAPP Addendum #2
PWSs must use the LCR Monitoring Form (LCRMF)
  Form #20683
  Customized/modified forms must be approved by TCEQ
Samples must be collected from the water system’s sample site pool
Samples must be labeled properly
LCRMF must be completed properly

## Slide 19: QAPP Addendum #2
Analysis
  Laboratory must meet EPA MRLs
    Lead – less than or equal to 0.005 mg/L
    Copper – less than or equal to 0.050 mg/L
  MRL verification
    LFB at the laboratory’s MRL
    Run with every preparation batch
  Do not report results below the MRL
    The PWSSP does not allow J flagged data

## Slide 20: QAPP Addendum #2
Reporting
  Electronic data submittal highly encouraged
    Labs should be submitting data weekly
    DO NOT hold all data to submit until after the end of the compliance period
  Paper reports
    Completed LCRMF
    Laboratory Chain of Custody (if applicable)
    Analytical test reports including QC

## Slide 21: QAPP Addendum #3
Guidance for the Analysis and Reporting of Water Quality Parameters (WQP) under the Lead and Copper Rule
Applies to PWSs and labs submitting data for compliance under the LCR (water quality parameters)
  Samples from public water systems
  Includes regulatory and program requirements
  Current Revision 1, effective 12/20/2017
  Includes TAC rule revision requirements effective 3/30/2017

## Slide 22: QAPP Addendum #3
Samples must be analyzed by a laboratory that is accredited in the drinking water matrix using a method acceptable to EPA OR approved by the Water Supply Division (WSD)
  Approved by WSD: temperature, pH, alkalinity, calcium, conductivity, ortho phosphate, silica
  Accredited by TCEQ: chloride, hardness, iron, manganese, sodium, sulfate, TDS
    QAPP only lists EPA allowed methods for which TCEQ offers accreditation

## Slide 23: QAPP Addendum #3
Samples must be collected in lab grade plastic bottles
  Volume should be sufficient to conduct all required analyses
Acid preservation should be done in the lab
    No later than 14 days after collection
Some analytes require thermal preservation
  Alkalinity, conductivity, sulfate, TDS, ortho phosphate

## Slide 24: QAPP Addendum #3
Field measurements
  pH and temperature must be measured and recorded in the field
  EPA allowed methods must be utilized
  Entity performing field measurements must complete and submit a laboratory approval form to the WSD

## Slide 25: QAPP Addendum #3
PWSs must use the Water Quality Parameter Monitoring Form (WQPMF)
  Form #20679
  Customized/modified forms must be approved by TCEQ
Samples must be labeled properly
WQPMF must be completed properly

## Slide 26: QAPP Addendum #3
Reporting
  Electronic data submittal highly encouraged
    Labs should be submitting data weekly
    DO NOT hold all data to submit until after the end of the compliance period
  Paper reports
    Completed WQPMF
    Laboratory Chain of Custody (if applicable)
    Analytical test reports including QC

## Slide 27: QAPP Addendum #3
Subcontracting/Pass-through
  Samples analyzed by multiple laboratories
  Initial (receiving) laboratory reports field measurements
  Results are reported by the lab that performed the analysis

## Slide 28: QAPP Addendum #4
Guidance for Analysis and Reporting Under the Revised Total Coliform Rule (RTCR)
  Applies to labs submitting data for compliance under RTCR
  Samples from public water systems
  Includes regulatory and program requirements
  Current Revision 1, effective 12/20/2017

## Slide 29: QAPP Addendum #4
Licensing Requirements
  Samples for community and non-transient non-community water systems MUST be collected by an individual with a valid water operators license
  Not required for transient systems
Field Measurements
  All samples must have a field measured chlorine residual
    DO NOT analyze, reject. Residual must not be filled in at the lab

## Slide 30: QAPP Addendum #4
Samples must be analyzed by a laboratory that is accredited in the drinking water matrix using a method acceptable to EPA
  Pg. 15, Table 1 lists EPA allowed drinking water methods
  Total coliform / E. coli
  Absence / Presence

## Slide 31: QAPP Addendum #4
Sample Containers
  Containers should be laboratory-supplied
  Batch tested for sterility if lab sterilized
  Tested for dechlorinating agent effectiveness
  Checked for accuracy of 100 mL mark
  Lot specific certificate of analysis required if containers obtained from a vendor

## Slide 32: QAPP Addendum #4
Sample Labels
  Adhesive or written directly on bottle
  Must include:
    PWS ID number
    Date & Time of sample collection
    Sampler’s initials
    Address/location of collection

## Slide 33: QAPP Addendum #4
Microbial Reporting Form (MRF)
  Use of unaltered form is mandatory if NOT submitting data electronically (E2)
  Modified forms may be used after TCEQ approval only if lab submits data electronically
  Form must capture:
    Sampler signature
    Lab chlorine check
    Legal statement

## Slide 34: QAPP Addendum #4
Sample Temperature
  Document temperature at time of receipt
    Recorded and corrected temperature
  Temperature measuring devices must be calibrated periodically
Chlorine Residual Lab Check
  Absence of a chlorine residual must be verified for every sample

## Slide 35: QAPP Addendum #4
Sample Rejection
  Insufficient/Incorrect documentation
    Corrections must be made by sampler, not the lab
    Field chlorine residuals must be measured and recorded in the field
  Sample Issues
    Broken in transit, exceeds hold time, frozen, leaked, etc.
    Lab measured chlorine residual
    Invalid results (turbid, too numerous to count, etc.)

## Slide 36: QAPP Addendum #4
Sample Rejection
  Notify PWS immediately
    Record notification on MRF
  PWS must recollect within 24 hours of notice
  Report rejected samples to TCEQ
    Ties back recollection to original
    Important in avoiding possible monitoring violations

## Slide 37: QAPP Addendum #4
Data submission
  Labs should be submitting data weekly
    Electronically through STEERS/E2 preferred
  DO NOT hold all data to submit until after the end of the compliance period
Microbial Reporting Form
  Labs should all now be using the new form or have implemented new requirements on customized forms
  Current version – 08/2017
  Instructions for PWSs and laboratories available online

## Slide 38: QAPP Addendum #4
Reporting Positive Samples
  Positive Result Report Form
    Email or Fax
    Current version – 08/2017
  Report on same day to TCEQ and PWS
    PWS must collect repeats

## Slide 39: QAPP Addendum #4
Sample Invalidation Requests
  PWS must complete and submit Total Coliform Positive Invalidation Request Form to TCEQ along with supporting documentation
    Current version – 10/24/2017
  Requests are assessed by the PWSSP QA Manager and approved by WSD management
  E. coli positive samples are not eligible for invalidation

## Slide 40: QAPP Overview
Labs may not make corrections to PWS portion of any reporting form (LCRMF, WQPMF, MRF)
  Corrections must be made by the sampler before relinquishment to lab
  Only TCEQ can authorize changes after analysis and reporting
    Evaluated on a case-by-case basis
    See QAPP for specific conditions

## Slide 41: QAPP Overview
Sample Receipt and Rejection
  Errors or omissions on reporting forms
  Improper bottle labeling
  Invalid/missing dates or times
  Missing PWS signature
  Broken/leaking containers
  Invalid containers
  Insufficient volume
  Exceeding hold time

## Slide 42: QAPP Overview
Corrective Actions
  Deviations from required protocols
  May be initiated by the lab or TCEQ
  Notify TCEQ of issue within 48 hours
    Corrective action report due within 14 days
    May require corrected data

## Slide 43: QAPP Overview
Laboratory Record Retention
  Easily accessible for five (5) years
  Applies to analyses under the LCR and RTCR
Reports should be coded following TCEQ Central File Room requirements
  See applicable QAPP for specifics

## Slide 44: QAPP Overview
Falsification and Fraud
  Falsification of the MRF or analytical results, or tampering with water samples used for compliance with the SDWA, is a crime punishable under state and/or federal law. [Texas Penal Code, Title 8, Chapter 37.10] By signing the MRF, the sample collector acknowledges that the water samples were collected according to the PWS’s established sample collection procedures, and that all information on the form is accurate. Evidence of falsification or fraud is turned over to the TCEQ Environmental Crimes Unit for investigation.

## Slide 45: EPA CMDP
Compliance Monitoring Data Portal (CMDP)
  Will enable PWSs and labs to report data electronically to TCEQ/EPA
  Will replace E2
  TCEQ working with EPA to ensure CROMEER and STEERS compatibility
  Testing anticipated in FY2019
More information:
  https://www.epa.gov/ground-water-and-drinking-water/compliance-monitoring-data-portal

## Slide 46: Questions?
Gary Regner
PWSS Program QA Manager
Gary.Regner@tceq.texas.gov
512/239-4528